## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 17
October 3, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover how to do math in the binary format and how to implement it in hardware
  Review Exam 1
  Decoder and Multiplexer
Homework 3 is due today at the beginning of the class
We will have quiz 3 today, which will be on lectures 10-15
We will have our Exam 1 on Friday, October 5, 2018, which will be on lecture 1-15
A sample exam with key is posted on Blackboard
Keys for HW 3 and Quiz 3 will post on Blackboard soon

## Slide 3
The First Midterm Exam will be on Friday, October 5
Lectures 1-15.

## Slide 4: Review of Computer Performance

## Slide 5: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 6: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 7: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 8: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 9: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 10: Review of Combinational Logic and Binary Math

## Slide 11: Different Logic Gates
A
B
AB
A
B
A+B
A
A’
A
B
(A.B)’
A
B
(A+B)’
(A+B)
A
B
AND
OR
NOT
NAND
NOR
XOR
You need to memorize their symbols and functions

## Slide 12: Boolean Algebra and Truth Table
Boolean algebra can be used to describe binary logic.
Boolean algebra operators (in the order of priority):
  () : Parenthesis
  ‘ : NOT
   : AND
  + : OR
Truth table can be used to represent input-output relations of a digital system.
You should be able to derive a truth table for a given logic circuit or Boolean algebra presentation and vice versa.

## Slide 13: Example: Truth Table, Boolean Algebra, and Digital Logic Circuit
A | B | C | BC | A+BC
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
C
B
BC
A
A+BC

## Slide 14: Constructing Gates
It turns out that, because the way a transistor works, the easiest gates to create are the NOT, NAND, and NOR gates

## Slide 15: Laws of Boolean Algebra
Identity law
  A + 0 = A
  A1 = A
Zero and One laws
  A + 1 = 1
  A 0 = 0
Inverse laws
  A + A’ = 1
  A A’ = 0
Commutative laws
  A + B = B + A
  A . B = B . A
Associative laws
  A + (B + C) = (A + B) + C
  A . (B . C) = A . (B . C)
Distributive laws
  A. (B + C) = (A.B) + (B.C)
  A+(B . C) = (A+B) . (A+C)
DeMorgan’s laws
  (AB)’=A’+B’
  (A+B)’=A’ B’

## Slide 16: Binary Math: Base Conversion
In everyday life, we used decimal base system which uses 10 as base.
In computer systems, binary base and other related bases such as hexadecimal base are used.
Example:
  3.2510 =11.012
  CF.116=11001111.00012
Note: In your exam, any conversion problem answer in format of M/N will receive no credit.

## Slide 17: Binary Numbers
Some terminology and units
  Bit (b): A single binary digit
  Nib: 4 bits
  Byte (B): 8-bits
  Word: A group of bits of any size (often 4 bytes).
  kb: 210 bits = 1024 bits (kB = 210 bytes)
  Mb: 220 bits =1,048,576 bits (MB = 220 bytes)
  Gb: 230 bits = 1,073,741,820 bits (GB = 230 bytes)
  MSB: Most significant bit (leftmost digit of binary #)
  LSB: Least significant bit (rightmost digit of bin. #)

## Slide 18: Binary to Decimal Conversion
···b3b2b1b0 (each bit bi is 0 or 1)
b0×20 + b1×21 + b2×22 + b3×23 + ···
= b0×1 + b1×2 + b2×4 + b3×8 + ···
Binary Number:
Its decimal value is:
Examples: 11102 Decimal value is:
11112 Decimal value is:
1100102 Decimal value is:
1111112 Decimal value is:
Check your understanding:
N bits  2N combinations  decimal numbers 0, 1, 2, 3, …, 2N - 1
The largest number: 11…112 = 2N-1 (decimal)
14
15
50
63
N bits, all ones

## Slide 19: Other Conversions
Convert decimal to hex
Use the successive division method described previously (for decimal to binary), but divide by 16 instead of 2.
Convert binary to hex
  A hex digit is equivalent to 4 bits.
  Divide binary number into groups of 4 bits, starting from the right.
  Convert each 4 bit group into one hex digit.
Convert hex to binary
  Convert each hex digit to its 4-bit binary equivalent.
  String the bits together.
Note: Computationally, it’s easy to convert between bases that are powers of 2, as indicated in the binary to hex conversion technique above.

## Slide 20: Other Conversions
Convert decimal to Octal
Use the successive division method described previously (for decimal to binary), but divide by 8 instead of 2.
Convert binary to Octal
  A octal digit is equivalent to 3 bits.
  Divide binary number into groups of 3 bits, starting from the right.
  Convert each 3 bit group into one octal digit.
Convert octal to binary
  Convert each octal digit to its 3-bit binary equivalent.
  String the bits together.
(examples on next slide)

## Slide 21: Fractions
Binary number: 0.b-1b-2b-3b-4···
Decimal value: b-1×2-1 + b-2×2-2 + b-3×2-3 + b-4×2-4 + ···
Binary to Decimal Conversion
Decimal to Binary Conversion: Successive multiplication by 2
Example: Decimal number 0.6875
Example: 0.1012 = 1×2-1 + 0×2-2 + 1×2-3 = 0.62510
0.68752 = 1.375  b-1 = 1 and 1.375-1 = 0.375
0.3752 = 0.75  b-2 = 0 and 0.75-0 = 0.75
0.752 = 1.5  b-3=1 and 1.5-1 = 0.5
0.52 = 1  b-4=1 and 1-1 = 0
Binary representation: 0.1011

## Slide 22: 1 Bit Full Adder Implementation
cin
b
a
s
Å
Å
=
cin
)
b
a
(
b
a
cout
Å
+
=
a
b
carry in
carry out
sum

## Slide 23: Binary Math: 2’s Complement
In binary world, people use 2’s complement to represent signed integer and implement subtraction.
The procedure of getting 2’s complement of a given number:
  Invert every bit
  Then add 1
For n bit signed integer, its representation is -2n-1 ~ 2n-1-1
  Example
    110011002 = - (00110100)2 = -5210
    100000002 = -12810

## Slide 24: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 25: Binary Math: Overflow Detection
Overflow happens when the calculation result is beyond the representation range for given number of bits.
Overflow might happen in one of following situations:
  Positive + Positive
  Negative + Negative
  Positive – Negative
  Negative – Positive
Important: You should determine whether an overflow happen by checking sign bits.
Example:
  Overflow: 11000000+10000000=01000000 (the extra carry out bit is discarded)
  Overflow: 01000000+01000000=10000000 (no extra bit)
  No Overflow 01000000+11000000=00000000 (the extra carry out bit is discarded)

## Slide 26: Good Luck!