## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 2
August 27, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We described different types of computers including different parts
We will begin to cover Instruction Set Architecture (ISA), computer model and performance today
Will learn:
  Computer model and Moore’s law
  Computer performance
Homework #1 will post on Blabckboard soon, which will due on Wednesday, Sept 5 at the beginning of the lecture
We will have our first Quiz on Friday, Sept 7, 2018, which will be on Lectures 1, 2, 3 and 4

## Slide 3: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface

## Slide 4: Instruction Set Architecture (ISA)
A very important abstraction
  interface between hardware and low-level software
  standardizes instructions, machine language bit patterns, etc.
Advantage: different implementations of the same architecture
Disadvantage: sometimes prevents using new innovations
Modern instruction set architectures:
  IA-32, PowerPC, MIPS, SPARC, ARM, and others

## Slide 5: MIPS Computer Simulator: SPIM
SPIM is a simulator developed for MIPS computer simulation.
You can download SPIM simulator PCSpim http://www.cs.wisc.edu/~larus/spim.html
We are going to cover how to use a SPIM simulator.

## Slide 6: Hierarchy of Computer Architecture
Coordination of many
levels (layers) of abstraction
Instruction Set
Architecture
I/O system
Processor
Compiler
Operating
System
(Mac OS X)
Application (ex: browser)
Digital Design
Circuit Design
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 7: The Instruction Set: a Critical Interface
instruction set
software
hardware

## Slide 8: What is Computer Architecture?
Computer Architecture = Instruction Set Architecture + Machine Organization + Hardware

## Slide 9: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 10: Levels of Representation (II)
Compiler
Assembler
temp=v[i]
v[i]=v[i+1]
v[i+1]=temp
add $2, $5, $5
add $2, $2, $2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
00a51020
00421020
00821020
8c620000
8cf20004
acf20000
ac620004
03e0008
One statement
=several
instructions
mostly
one-to-one
Which one will be more difficult to design: Complier or Assembler?

## Slide 11: A MIPS Computer Architecture:

## Slide 12: Hardware Components of any Computer
Processor
(active)
Computer
Control
Unit
Datapath
Memory
(passive)
(where
programs,
data
live when
running)
Devices
Input
Output
Keyboard, Mouse, etc.
Display, Printer, etc.
Disk
Five classic components of all computers:
1. Control Unit; 2. Datapath; 3. Memory; 4. Input; 5. Output
}
Processor

## Slide 13: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 14: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers

## Slide 15: The Von-Neumann Computer Model
Partitioning of the computing engine into components:
  Central Processing Unit (CPU):
    Control Unit (instruction decode, sequencing of operations),
    Datapath (registers, arithmetic and logic unit, buses).
  Memory: Instruction (program) and operand (data) storage.
  Input/Output (I/O).
-
Memory
(instructions,
data)
Control
Datapath
registers
ALU, buses
CPU
Computer System
Input
Output
I/O Devices

## Slide 16: Harvard and von Neumann Architecture
CPU
Data
Memory
Code
Memory
Harvard Architecture
CPU
Memory
(Data
and Code)
Von Neumann Architecture

## Slide 17: Mechanical Computer: Babbage Difference Engine (1822)

## Slide 18: Historical Perspective
ENIAC built in World War II was the first general purpose computer
  Used for computing artillery firing tables
  80 feet long by 8.5 feet high and several feet wide
  Each of the twenty 10 digit registers was 2 feet long
  Used 18,000 vacuum tubes and Weighed 80 tons
  Performed 5000 additions per second (3 GHz Pentium 4 can do about 600 millions of additions per second)

## Slide 19: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2005 | Ultra large scale IC | 6,200,000,000 | 
DRAM capacity

## Slide 20: Computer Technology – Dramatic Change!
Memory
  DRAM capacity: 2x / 2 years (since ‘96); 64X size improvement in last decade.
Processor
  Speed 2x / 1.5 years (since ‘85); 100X performance in last decade.
Disk
  Capacity: 2x / 1 year (since ‘97) 250X size in last decade.
How long will Moore’s Law last?

## Slide 21: What Can we Learn From Moore’s Law
Rapid Improvement is the key in computer industry!

## Slide 22: Performance
Measure, Report, and Summarize
Make intelligent choices
See through the marketing hype
Key to understanding underlying organizational motivation
  Why is some hardware better than others for different programs?
  What factors of system performance are hardware related? (e.g., Do we need a new machine, or a new operating system?)
  How does the machine's instruction set affect performance?

## Slide 23: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 24: Defining Performance
Which airplane has the best performance?

## Slide 25: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 26: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 27: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent for processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 28: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 29: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count