## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 28 and 29
November 7, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will CONTINUE our coverage on MIPS assembly language
We will learn followings today:
  Memory vs. Register
  MIPS Register Conventions
  MIPS Control Instruction
We will learn how to write code in MIPS simulator
Quiz 6 will be on Wednesday, Nov 14, which will cover Lectures 25-30
We will have Exam 2 on Friday, Nov 16, which will cover Lectures 16-30
A sample Exam 2 will post on Blackboard soon

## Slide 3: Review: MIPS Data Transfer Instructions
We learned the following two MIPS data transfer instructions:
Load word
lw $s1, 100($s2) $s1 = Memory[$s2+100]
Save word sw $s1, 100($s2) Memory[$s2+100] = $s1

## Slide 4: MIPS Data Transfer Instructions Example
C code: A[12] = h + A[8]; MIPS code: lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
$s3: base address (as called index register)
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory! Can’t write: add 48($s3), $s2, 32($s3)
Word Address
Byte Address

## Slide 5: Exercise: Data Transfer Instructions
C code: A[100] = h + A[100]; MIPS code: ?
  $t0: temporary register to store A[100]
  $t1: index register
  $s2 corresponds to h

## Slide 6: Machine Language Type of Load/Store Instructions
Example: lw $t0, 32($s2) 35 18 8 32 op rs rt 16 bit number
Example: sw $t0, 32($s2) 43 18 8 32 op rs rt 16 bit number

## Slide 7: Pointers v. Values
Key Concept: A register can hold any 32-bit value. That value can be a (signed) int, an unsigned int, a pointer (memory address), and so on
If you write add $t2,$t1,$t0 then $t0 and $t1 better contain values
If you write lw $t2,0($t0) then $t0 better contain a pointer
Don’t mix these up!

## Slide 8: Addressing: Byte vs. Word
Every word in memory has an address, similar to an index in an array
Early computers numbered words like C numbers elements of an array:
  Memory[0], Memory[1], Memory[2], …
Called the “address” of a word
Computers needed to access 8-bit bytes as well as words (4 bytes/word)
Today machines address memory as bytes, (i.e.,“Byte Addressed”) hence 32-bit (4 byte) word addresses differ by 4
  Memory[0], Memory[4], Memory[8], …

## Slide 9: Compilation with Memory
What offset in lw to select A[5] in C?
4x5=20 to select A[5]: byte v. word
Compile by hand using registers: g = h + A[5];
  g: $s1, h: $s2, $s3:base address of A
1st transfer from memory to register:
lw $t0,20($s3) # $t0 gets A[5]
  Add 20 to $s3 to select A[5], put into $t0
Next add it to h and place in g add $s1,$s2,$t0 # $s1 = h+A[5]

## Slide 10: Notes about Memory
Pitfall: Forgetting that sequential word addresses in machines with byte addressing do not differ by 1.
  Many an assembly language programmer has toiled over errors made by assuming that the address of the next word can be found by incrementing the address in a register by 1 instead of by the word size in bytes.
  So remember that for both lw and sw, the sum of the base address and the offset must be a multiple of 4 (to be word aligned)

## Slide 11: More Notes about Memory: Alignment
MIPS requires that all words start at byte addresses that are multiples of 4 bytes
0 1 2 3
Aligned
Not
Aligned
Called Alignment: objects must fall on address that is multiple of their size.
0, 4, 8, or Chex
Last hex digit of address is:
1, 5, 9, or Dhex
2, 6, A, or Ehex
3, 7, B, or Fhex

## Slide 12: Registers vs. Memory
What if more variables than registers?
  Compiler tries to keep most frequently used variable in registers
  Less common in memory: spilling
    A "spilled variable" is a variable in main memory rather than in a CPU register.
Why only 32 registers?
  Smaller is faster
Why not keep all variables in memory?
  registers are faster than memory
  Registers more versatile:
    MIPS arithmetic instructions can read 2, operate on them, and write 1 per instruction
    MIPS data transfer only read or write 1 operand per instruction, and no operation

## Slide 13: So far we’ve learned
Memory is byte-addressable, but lw and sw access one word at a time.
A pointer (used by lw and sw) is just a memory address, so we can add to it or subtract from it (using offset).
We covered the following MIPS instructions so far.
Instruction Meaning Arithmetic:
add $s1, $s2, $s3 $s1 = $s2 + $s3 sub $s1, $s2, $s3 $s1 = $s2 – $s3
addi $s1, $s2, 100 $s1 = $s2 + 100
Data Transfer
lw $s1, 100($s2) $s1 = Memory[$s2+100] sw $s1, 100($s2) Memory[$s2+100] = $s1

## Slide 14: MIPS Register Conventions
Note: Register 1 ($at) reserved for assembler, 26-27 for operating system

## Slide 15: MIPS Control Instruction I: Conditional Branch
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions:
bne $t0, $t1, Label : if ($t0!=$t1) go to Label beq $t0, $t1, Label : if ($t0==$t1) go to Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....

## Slide 16: MIPS Control Instruction II: Unconditional Jump
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Technically, it’s the same as:
  beq $0,$0,label
  since it always satisfies the condition.

## Slide 17: Example: Compiling C if into MIPS (1/2)
Compile by hand
  if (i == j) f=g+h; else f=g-h;
Use this mapping: f: $s0 g: $s1 h: $s2 i: $s3 j: $s4
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j