## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 3
August 29, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We discussed Computer Model and Moore’s law.
Will continue to cover computer performance today
Will learn:
  More about Computer performance
  Integrated Circuit (IC) Cost
  Logic gates and expression
Homework #1 will post on blackboard soon, which will due on Wednesday, Sept. 5 at the beginning of the lecture (Hard Copy)
We will have our first Quiz on Friday, Sept. 9, 2018, which will be on Lectures 1, 2, 3 and 4

## Slide 3: Review: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 4: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 5: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 6: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which computer is faster, and by how much?
A is faster…
…by this much

## Slide 7: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 8: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 9: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 10
Intel CPU Trends

## Slide 11: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 12: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 13: Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency

## Slide 14: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 15: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 16: Summary
Today, we finished our coverage on computer performance.
We will begin to cover IC and logic gates.
HW 1 will post on canvas soon.