## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 32
November 14, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
In the past few weeks, we mainly focused on MIPS assembly language.
We will review Midterm Exam 2 first
HW #6 is due today
We will have quiz 6 today which will cover lectures 25-30
We will have Midterm Exam 2 on Friday, November 16 which will be on lectures 16-30
A sample midterm exam 2 is posted on Blackboard
SDS center for additional time for Exam
No class on Monday, Nov 19

## Slide 3: The Second Midterm Exam
We will have our second midterm exam this week on November 16 (Friday)
  Coverage: All materials covered up to Nov. 9 (Lecture Notes 16-30.)
One more quiz will be given before the first midterm
  Quiz #6: Today (on Lectures- 25, 26, 27, 28, 29 and 30)
A sample exam is posted on Blackboard
A memory less calculator is allowed in the exam

## Slide 4: Review of Midterm Exam 2

## Slide 5: Multiplication and Division by Shifting Bits
We will cover multiplication in great details later. However, some simple multiplication can be accomplished simply by shifting the bit sequence.

## Slide 6: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000

## Slide 7: Shifting and Multiplication
Shift Left a binary number by i bits will give the same result as multiplying by 2i. (True or False)
Shift Right a binary number by i bits will give the same result as dividing by 2i. (True or False)

## Slide 8: Decoder
Popular combinational logic building block, in addition to logic gates
Collection of logic gates which are arranged in a specific way that converts input binary number to one high output
2-input decoder: four possible input binary numbers... So has four outputs, one for each possible input binary number

## Slide 9: Building of 4-to-1-line Multiplexer
2-to-22-line decoder
22 ´ 2 AND-OR

## Slide 10: The ALU Diagram
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
ALU 0~30
ALU 31
Can this ALU implement a NAND function?

## Slide 11: Introduction to Sequential Circuits
A Sequential circuit contains:
  Storage elements: Latches or Flip-Flops
  Combinatorial Logic:
    Implements a multiple-output switching function
    Inputs are signals from the outside.
    Outputs are signals to the outside.
    Other inputs, State or Present State, are signals from storage elements.
    The remaining outputs, Next State are inputs to storage elements.
Combina-tional
Logic
Storage Elements
Inputs
Outputs
State
Next
State

## Slide 12: The Latch Timing Problem (continued)
Consider the following circuit:
Suppose that initially Y = 0.
As long as C = 1, the value of Y continues to change!
The changes are based on the delay present on the loop through the connection from Y back to Y.
This behavior is clearly unacceptable.
Desired behavior: Y changes only once per clock pulse
Clock
Y
C
D
Q
Q
Y
Clock

## Slide 13: Storage Element’s Timing Model
Setup Time: Input must be stable BEFORE trigger clock edge
Hold Time: Input must REMAIN stable after trigger clock edge
Clock-to-Q time:
  Output cannot change instantaneously at the trigger clock edge
  Similar to delay in logic gates, two components:
    Internal Clock-to-Q
    Load dependent Clock-to-Q
Typical for class: 1ns Setup, 0.5ns Hold
D
Q
D
Don’t Care
Don’t Care
Clk
Unknown
Q
Setup
Hold
Clock-to-Q
Notes: So far we have been looking at combinational logic, let’s look at the timing characteristic of a storage element.
The storage element you will use is a D type flip-flop trigger on the negative clock edge.
In order for the data to latch into the flip flop correctly, the input must be stable slightly before the falling edge of the clock. This time is called the Setup time.
After the clock edge has arrived, the data must remain stable for a short amount of time AFTER the trigger clock edge. This is called the hold time.
The output cannot change instantaneously at the trigger clock edge. The time it takes for the output to change to its new value after the clock is called the Clock-to-Q time.
Similar to delay in logic gates, the Clock-to-Q time has two components:
(a) The internal Clock-to-Q time: the time it takes the output to change if output load is zero.
(b) And the load dependent Clock-to-Q time.
+2 = 50 min. (Y:30)

## Slide 14: Machine Format
Our processor’s machine code format is given below
  [load, regad1, regad2, des_regad, aluop]
    load signal: 1 (read from external input), 0 (read from ALU)
    regad1: the address of the register for the ALU input 1
    regad2: the address of the register for the ALU input 2
    des_regad: the address of the destination register which data is written into
    aluop: the ALU function selection
There are 16 registers and 8 ALU functions.
Question: Based on the above description of the processor, how many bits each command should have?

## Slide 15: MIPS Assembly Language
We’ll be working with the MIPS instruction set architecture
  developed in 1985
  means “Microprocessor without Interlocked Pipeline Stages”
  similar to other architectures developed since the 1980's
  almost 100 million MIPS processors manufactured in 2002
  used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, …
  a Reduced Instruction Set Computer (RISC) Assembly Language
Instruction Category:
  Arithmetic: Add, Subtract,…
  Data Transfer: Load Word,…
  Logical: And, Or,…
  Conditional Branch: Branch on Equal,…
  Unconditional Jump: Jump

## Slide 16: Assembly Variables: Registers Cont..
Registers are numbered from 0 to 31
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31

## Slide 17: Assembly Variables: Registers Cont…
By convention, each register also has a name to make it easier to code
For now:
  $16 - $23  $s0 - $s7
  (correspond to C variables)
  $8 - $15  $t0 - $t7
  (correspond to temporary variables)
In general, use names to make your code more readable

## Slide 18: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, the registers have no type; operation determines how register contents are treated

## Slide 19: MIPS Registers
USE Number Name
The constant 0 $0 $zero
Reserved for Assembler $1 $at
Return Values $2-$3 $v0-$v1
Arguments $4-$7 $a0-$a3
Temporary $8-$15 $t0-$t7
Saved Temporaries $16-$23 $s0-$s7
Temporary $24-$25 $t8-$t9
Used by Kernel $26-$27 $k0-$k1
Global Pointer $28 $gp
Stack Pointer $29 $sp
Frame Pointer $30 $fp
Return Address $31 $ra

## Slide 20: Registers vs. Memory
Arithmetic instructions operands must be registers, — only 32 registers provided
Which computer components do registers belongs to?
Compiler associates variables with registers
What about programs with lots of variables?
Processor
I/O
Control
Datapath
Memory
Input
Output

## Slide 21: Comments in MIPS Programs
You can use comments to make your code more readable.
Hash (#) is used for MIPS comments
  anything from hash mark to end of line is a comment and will be ignored
Note: Different from C.
  C comments have format /* comment */ so they can span many lines

## Slide 22: MIPS Addition and Subtraction (1/4)
Syntax of Instructions:
  1 2, 3, 4
  where:
  1) operation by name
  2) operand getting result (“destination”)
  3) 1st operand for operation (“source1”)
  4) 2nd operand for operation (“source2”)
Syntax is rigid:
  1 operator, 3 operands
  Operand order is fixed (destination first)
  Why? Keep Hardware simple via regularity
Design Principle: simplicity favors regularity.

## Slide 23: Addition and Subtraction of Integers (2/4)
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where MIPS registers $s0,$s1,$s2 are associated with C variables a, b, c
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where MIPS registers $s3,$s4,$s5 are associated with C variables d, e, f

## Slide 24: Addition and Subtraction of Integers (3/4)
How do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
Notice: A single line of C may break up into several lines of MIPS.
Notice: Everything after the hash mark on each line is ignored (comments)

## Slide 25: Addition and Subtraction of Integers (4/4)
How do we do this?
f = (g + h) - (i + j);
Use intermediate temporary register
  add $t0,$s1,$s2 # temp = g + h
  add $t1,$s3,$s4 # temp = i + j
  sub $s0,$t0,$t1 # f=(g+h)-(i+j)

## Slide 26: Immediates
Immediates are numerical constants.
They appear often in code, so there are special instructions for them.
Add Immediate:
  addi $s0,$s1,10 (in MIPS)
  f = g + 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
Syntax similar to add instruction, except that last argument is a number instead of a register.

## Slide 27: Immediates
There is no Subtract Immediate in MIPS:
Limit types of operations that can be done to absolute minimum
  if an operation can be decomposed into a simpler operation, don’t include it
  addi …, -X = subi …, X => so no subi
addi $s0,$s1,-10 (in MIPS)
  f = g - 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g

## Slide 28: Register Zero
One particular immediate, the number zero (0), appears very often in code.
So we define register zero ($0 or $zero) to always have the value 0; eg
  add $s0,$s1,$zero (in MIPS)
  f = g (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
defined in hardware, so an instruction
  add $zero,$zero,$s0
will not do anything!

## Slide 29: Review: MIPS Instruction Format
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide

## Slide 30: Machine Language: R-Type
Numeric version of instructions is called machine language
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers, $t0=8, $s1=17, $s2=18
Instruction Format: add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
Can you guess what the field names stand for?
Notes: Board work: Binary Numbers

## Slide 31: Machine Language: I-Type
Consider the addi instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for immediates
  other format was R-type for register
Example: addi $s1, $s2, 100 8 18 17 100 op rs rt 16 bit number

## Slide 32: MIPS Fields
op: Basic operation of the instruction, opcode
rs: The first register source operand
rt: The second register source operand
rd: The register destination operand.
shamt: Shift amount
funct: Function

## Slide 33: Assembly Operands: Memory
C variables map onto registers; what about large data structures like arrays?
1 of 5 components of a computer: memory contains such data structures
But MIPS arithmetic instructions only operate on registers, never directly on memory.
Data transfer instructions transfer data between registers and memory:
  Memory to register
  Register to memory

## Slide 34: Anatomy: 5 components of any Computer
Personal Computer
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
Load (from)
Store (to)
These are “data transfer” instructions…
Registers are in the datapath of the processor; if operands are in memory, we must transfer them to the processor to operate on them, and then transfer back to memory when done.
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 35: Data Transfer: Memory to Reg (1/4)
To transfer a word of data, we need to specify two things:
  Register: specify this by # ($0 - $31) or symbolic name ($s0,…, $t0, …)
  Memory address: more difficult
    Think of memory as a single one-dimensional array, so we can address it simply by supplying a pointer to a memory address.
    Other times, we want to be able to offset from this pointer.
Remember: “Load FROM memory”

## Slide 36: Data Transfer: Memory to Reg (2/4)
To specify a memory address to copy from, specify two things:
  A register containing a pointer to memory
  A numerical offset (in bytes)
The desired memory address is the sum of these two values.
Example: 8($t0)
  specifies the memory address pointed to by the value in $t0, plus 8 bytes

## Slide 37: Data Transfer: Memory to Reg (3/4)
Load Instruction Syntax:
  1 2, 3(4)
  where
  1) operation name
  2) register that will receive value
  3) numerical offset in bytes
  4) register containing pointer to memory
MIPS Instruction Name:
  lw (meaning Load Word, so 32 bits or one word are loaded at a time)

## Slide 38: Data Transfer: Memory to Reg (4/4)
Example: lw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then load the value from the memory pointed to by this calculated sum into register $t0
Notes:
  $s0 is called the base register
  12 is called the offset
  offset is generally used in accessing elements of array or structure: base reg points to beginning of array or structure
Data flow

## Slide 39: Data Transfer: Reg to Memory
Also want to store from register into memory
  Store instruction syntax is identical to Load’s
MIPS Instruction Name:
sw (meaning Store Word, so 32 bits or one word are loaded at a time)
Example: sw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then store the value from register $t0 into that memory address
Remember: “Store INTO memory”
Data flow

## Slide 40: System Calls
SPIM provides a small set of operating-system-like services through the system call (syscall) instruction.
To request a service, a program load the system call code into the register $v0 and arguments into registers $a0-$a3.

## Slide 41: Pseudoinstruction
The following two instructions are not real MIPS instruction. They can be implemented with real MIPS instruction though. Therefore, they are called “pseudoinstructions.” They are created for the convenience of programmers.
li $reg, imm (load immediate)
  - $reg=imm
la $reg address (load address)
  - $reg=address
To use pseudoinstructions, you need to specify that pseudoinstrcutions is allowed in the setting of SPIM simulator.

## Slide 42: Assembler Directives
Assembler directives begin a period.
Assembler directives tell the assembler how to translate a program but do not produce machine code for itself.
Example:
  .globl sym: declare that label sym is global and can be referred from other files.
  .text: subsequent items are put in the user segment. In SPIM, these items may only be instructions or words.
  .data: declare that subsequent items are stored in the data segment.
  .asciiz str: store the string str in memory and null-terminated

## Slide 43: The First Program: Hello World
.text
.globl main
main:
li $v0, 4
la $a0, str
syscall # print string
li $v0, 10
syscall # exit (you must use syscall #10 to exit)
.data
str: .asciiz "Hello World!!!"

## Slide 44: MIPS Data Transfer Instructions Example
C code: A[12] = h + A[8]; MIPS code: lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
$s3: base address (as called index register)
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory! Can’t write: add 48($s3), $s2, 32($s3)
Word Address
Byte Address

## Slide 45: Pointers v. Values
Key Concept: A register can hold any 32-bit value. That value can be a (signed) int, an unsigned int, a pointer (memory address), and so on
If you write add $t2,$t1,$t0 then $t0 and $t1 better contain values
If you write lw $t2,0($t0) then $t0 better contain a pointer
Don’t mix these up!

## Slide 46: Addressing: Byte vs. Word
Every word in memory has an address, similar to an index in an array
Early computers numbered words like C numbers elements of an array:
  Memory[0], Memory[1], Memory[2], …
Called the “address” of a word
Computers needed to access 8-bit bytes as well as words (4 bytes/word)
Today machines address memory as bytes, (i.e.,“Byte Addressed”) hence 32-bit (4 byte) word addresses differ by 4
  Memory[0], Memory[4], Memory[8], …

## Slide 47: Compilation with Memory
What offset in lw to select A[5] in C?
4x5=20 to select A[5]: byte v. word
Compile by hand using registers: g = h + A[5];
  g: $s1, h: $s2, $s3:base address of A
1st transfer from memory to register:
lw $t0,20($s3) # $t0 gets A[5]
  Add 20 to $s3 to select A[5], put into $t0
Next add it to h and place in g add $s1,$s2,$t0 # $s1 = h+A[5]

## Slide 48: Notes about Memory
Pitfall: Forgetting that sequential word addresses in machines with byte addressing do not differ by 1.
  Many an assembly language programmer has toiled over errors made by assuming that the address of the next word can be found by incrementing the address in a register by 1 instead of by the word size in bytes.
  So remember that for both lw and sw, the sum of the base address and the offset must be a multiple of 4 (to be word aligned)

## Slide 49: More Notes about Memory: Alignment
MIPS requires that all words start at byte addresses that are multiples of 4 bytes
0 1 2 3
Aligned
Not
Aligned
Called Alignment: objects must fall on address that is multiple of their size.
0, 4, 8, or Chex
Last hex digit of address is:
1, 5, 9, or Dhex
2, 6, A, or Ehex
3, 7, B, or Fhex

## Slide 50: Registers vs. Memory
What if more variables than registers?
  Compiler tries to keep most frequently used variable in registers
  Less common in memory: spilling
    A "spilled variable" is a variable in main memory rather than in a CPU register.
Why only 32 registers?
  Smaller is faster
Why not keep all variables in memory?
  registers are faster than memory
  Registers more versatile:
    MIPS arithmetic instructions can read 2, operate on them, and write 1 per instruction
    MIPS data transfer only read or write 1 operand per instruction, and no operation

## Slide 51: MIPS Control Instruction I: Conditional Branch
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions:
bne $t0, $t1, Label : if ($t0!=$t1) go to Label beq $t0, $t1, Label : if ($t0==$t1) go to Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....

## Slide 52: MIPS Control Instruction II: Unconditional Jump
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Technically, it’s the same as:
  beq $0,$0,label
  since it always satisfies the condition.

## Slide 53: Example: Compiling C if into MIPS (1/2)
Compile by hand
  if (i == j) f=g+h; else f=g-h;
Use this mapping: f: $s0 g: $s1 h: $s2 i: $s3 j: $s4
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j

## Slide 54: Example: Compiling C if into MIPS (2/2)
Final compiled MIPS code:
beq $s3,$s4,True # branch i==j sub $s0,$s1,$s2 # f=g-h(false) j Fin # goto Fin True: add $s0,$s1,$s2 # f=g+h (true) Fin:
Note: Compiler automatically creates labels to handle decisions (branches). Generally not found in HLL code.
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j
Compile by hand
  if (i == j) f=g+h; else f=g-h;

## Slide 55: Inequalities in MIPS (1/5)
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Create a MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning: reg1 = (reg2 < reg3);
  if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  Usually, “set” means “set to 1”, “reset” means “set to 0”.
Same thing…

## Slide 56: Inequalities in MIPS (2/5)
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$0,Less # goto Less # if $t0!=0 # (if (g<h)) Less:
Branch if $t0 != 0  (g < h)
Register $0 always contains the value 0, so bne and beq often use it for comparison after an slt instruction.
A slt  bne pair means if(… < …)goto…

## Slide 57: Inequalities in MIPS (3/5)
We covered two pseudo instructions, li and la, in our SPIM tutorial session.
The following pseudo instruction is also useful:
"blt $s1, $s2, Label“
    called “branch on less than”
    can now build general control structures
Note that the assembler needs a register ($at: assembler temporary) to do this,
  there are policy of use conventions for registers
Notes: Board work: Binary Numbers

## Slide 58: Inequalities in MIPS (4/5)
Now, we can implement <, but how do we implement >, ≤ and ≥ ?
We could add 3 more instructions, but:
  MIPS goal: Simpler is Better
Can we implement ≤ in one or more instructions using just slt and the branches?
What about >?
What about ≥?

## Slide 59: Inequalities in MIPS (5/5)
if (g >= h) goto Loop #g:$s0, h:$s1
Loop: . . .
slt $t0,$s0,$s1 # $t0 = 1 if # $s0<$s1 (g<h) beq $t0,$0,Loop # goto Loop # if $t0==0 # if (g  h))
C
M I P S
A slt  beq pair means if(… ≥ …)goto…

## Slide 60: Example: The C Switch Statement (1/3)
Choose among four alternatives depending on whether k has the value 0, 1, 2 or 3. Compile this C code: switch (k) { case 0: f=i+j; break; /* k=0 */ case 1: f=g+h; break; /* k=1 */ case 2: f=g–h; break; /* k=2 */ case 3: f=i–j; break; /* k=3 */ }

## Slide 61: Example: The C Switch Statement (2/3)
This is complicated, so simplify.
Rewrite it as a chain of if-else statements, which we already know how to compile:
  if(k==0) f=i+j; else if(k==1) f=g+h; else if(k==2) f=g–h; else if(k==3) f=i–j;
Use this mapping:
  f:$s0, g:$s1, h:$s2, i:$s3, j:$s4, k:$s5

## Slide 62: Example: The C Switch Statement (3/3)
Final compiled MIPS code: bne $s5,$0,L1 # branch k!=0 add $s0,$s3,$s4 #k==0 so f=i+j j Exit # end of case so Exit L1: addi $t0,$s5,-1 # $t0=k-1 bne $t0,$0,L2 # branch k!=1 add $s0,$s1,$s2 #k==1 so f=g+h j Exit # end of case so Exit L2: addi $t0,$s5,-2 # $t0=k-2 bne $t0,$0,L3 # branch k!=2 sub $s0,$s1,$s2 #k==2 so f=g-h j Exit # end of case so Exit L3: addi $t0,$s5,-3 # $t0=k-3 bne $t0,$0,Exit # branch k!=3 sub $s0,$s3,$s4 #k==3 so f=i-j Exit:

## Slide 63: MIPS Control Instructions Syntax
Instruction Meaning bne $s4,$s5,L Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label slt $s1,$s2,$s3 if ($s2<$s3) $s1=1; else $s1=0
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 64: MIPS Logical Operations
Three basic logical operators in MIPS:
  AND: outputs 1 only if both inputs are 1
  OR: outputs 1 if at least one input is 1
  NOR: outputs 1 if both inputs are 0
Truth Table: standard table listing all possible combinations of inputs and resultant output for each. E.g.,
A | B | A AND B | A OR B | A NOR B
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 65: Logical Instruction Syntax
R-Format
op rs rt rd shamt funct
I-Format
op rs rt 16 bit number
  $s1 = $s2&$s3: and $s1, $s2, $s3
  $s1 = $s2|$3: or $s1, $s2, $s3
  $s1 = ~($s2|$s3): nor $s1, $s2, $s3
There is another important logical function, NOT.
NOT (1) = 0 and NOT (0) = 1.
How to implement NOT function (~) with MIPS instruction?

## Slide 66: Exercise: Implement NOT function with NOR instruction
A NOR 0 = NOT (A)
Nor $s1, $s2, $zero : $s1=~$s2

## Slide 67: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000
  What arithmetic effect does shift left have?

## Slide 68: Shift Instruction Syntax
MIPS shift instructions:
1. sll (shift left logical): shifts left and fills emptied bits with 0s
2. srl (shift right logical): shifts right and fills emptied bits with 0s
Machine version of “sll $t2, $s0, 4”:
op rs rt rd shamt funct
0 0 16 10 4 0

## Slide 69: Loops in C/Assembly (1/3)
Simple loop in C; A[] is an array of integers
  do {g = g + A[i];
  i = i + j; } while (i != h);
Rewrite this as:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5

## Slide 70: Loops in C/Assembly (2/3)
Final compiled MIPS code:
Loop: sll $t1,$s3,2 #$t1= 4*i add $t1,$t1,$s5 #$t1=addr A lw $t1,0($t1) #$t1=A[i] add $s1,$s1,$t1 #g=g+A[i] add $s3,$s3,$s4 #i=i+j bne $s3,$s2,Loop# goto Loop # if i!=h
Original code:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5
Notes: Do goto first
Then I = I + J
Then 1st 4

## Slide 71: So far we’ve learned:
Arithmetic:
add $s1, $s2, $s3 $s1 = $s2 + $s3 sub $s1, $s2, $s3 $s1 = $s2 – $s3
addi $s1, $s2,100 $s1 = $s2 + 100
Data Transfer
lw $s1, 100($s2) $s1 = Memory[$s2+100] sw $s1, 100($s2) Memory[$s2+100] = $s1
Control
bne $s4,$s5,Label Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,Label Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
slt $s1,$s2,$s3 if ($s2<$s3) $s1=1; else $s1=0
Logical and $s1, $s2, $s3 $s1=$s2&$S3
or $s1, $s2, $s3 $s1=$s2|$s3
nor $s1, $s2, $s3 $s1=~($s2|$s3)
sll $s1, $s2, 10 $s1=$s2<<10
sr1 $s1, $s2, 10 $s1=$s2>>10