## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 4
August 31, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We discussed Computer performance.
Will continue to cover computer performance today
Will learn:
  Integrated Circuit (IC) Cost
  Logic gates and expression
Homework #1 is posted on blackboard, which will due on Wednesday, Sept. 5 at the beginning of the lecture (Hard Copy)
We will have our first Quiz on Friday, Sept. 9, 2018, which will be on Lectures 1, 2, 3 and 4
No class on Monday, Sept. 3, 2018, labor day

## Slide 3: Review: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 4: Review: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 5: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 6: Intel core i7 Wafer
i7: 300mm (12 inch) wafer, 280 chips, 32nm technology
AMD X2: 300nm, 117 chips, 90nm technology
X4: 45nm technology

## Slide 7: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 8: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Cooperative (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)

## Slide 9: CINT2006 for Opteron X4 2356
Name | Description | IC×109 | CPI | Tc (ns) | Exec time | Ref time | SPECratio
perl | Interpreted string processing | 2,118 | 0.75 | 0.40 | 637 | 9,777 | 15.3
bzip2 | Block-sorting compression | 2,389 | 0.85 | 0.40 | 817 | 9,650 | 11.8
gcc | GNU C Compiler | 1,050 | 1.72 | 0.47 | 24 | 8,050 | 11.1
mcf | Combinatorial optimization | 336 | 10.00 | 0.40 | 1,345 | 9,120 | 6.8
go | Go game (AI) | 1,658 | 1.09 | 0.40 | 721 | 10,490 | 14.6
hmmer | Search gene sequence | 2,783 | 0.80 | 0.40 | 890 | 9,330 | 10.5
sjeng | Chess game (AI) | 2,176 | 0.96 | 0.48 | 37 | 12,100 | 14.5
libquantum | Quantum computer simulation | 1,623 | 1.61 | 0.40 | 1,047 | 20,720 | 19.8
h264avc | Video compression | 3,102 | 0.80 | 0.40 | 993 | 22,130 | 22.3
omnetpp | Discrete event simulation | 587 | 2.94 | 0.40 | 690 | 6,250 | 9.1
astar | Games/path finding | 1,082 | 1.79 | 0.40 | 773 | 7,020 | 9.1
xalancbmk | XML parsing | 1,058 | 2.70 | 0.40 | 1,143 | 6,900 | 6.0
Geometric mean |  |  |  |  |  |  | 11.7
High cache miss rates

## Slide 10: SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)
  Where, ssj_opsi is performance at each 10% increment and poweri is power consumed at each performance level.

## Slide 11: SPECpower_ssj2008 for X4
Target Load % |  | Performance (ssj_ops/sec) |  | Average Power (Watts) | 
100% |  | 231,867 |  | 295 | 
90% |  | 211,282 |  | 286 | 
80% |  | 185,803 |  | 275 | 
70% |  | 163,427 |  | 265 | 
60% |  | 140,160 |  | 256 | 
50% |  | 118,324 |  | 246 | 
40% |  | 920,35 |  | 233 | 
30% |  | 70,500 |  | 222 | 
20% |  | 47,126 |  | 206 | 
10% |  | 23,066 |  | 180 | 
0% |  | 0 |  | 141 | 
Overall sum |  | 1,283,590 |  | 2,605 | 
∑ssj_ops/ ∑power |  |  |  | 493 | 

## Slide 12: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in speed of multiplication performance to get 5× faster overall?
Corollary: make the common case fast

## Slide 13: Amdahl’s Law in Reality

## Slide 14: Fallacy: Low Power at Idle
Look back at X4 power benchmark
  At 100% load: 295W
  At 50% load: 246W (83%)
  At 10% load: 180W (61%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load

## Slide 15: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU

## Slide 16: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance

## Slide 17: In Lecture Review
We finished our coverage on Chapter 1
We will have Quiz 1 on Friday, September 7
We will begin our coverage on Digital logic gates and expression now

## Slide 18: ALU in a MIPS Computer
ALU

## Slide 19: Digital Logic
An signal can be defined as an information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
Two level, or binary values are the most prevalent values in modern computers.
Binary values are represented abstractly by:
  digits 0 and 1
  words (symbols) False (F) and True (T)
  words (symbols) Low (L) and High (H)
  and words On and Off.

## Slide 20: Signal Example – Physical Quantity: Voltage
Threshold Region
5.0
4.0
3.0
2.0
1.0
0.0
Volts
HIGH
LOW
HIGH
LOW
OUTPUT
INPUT
Notes: The HIGH range typically corresponds to binary 1 and LOW range to binary 0. The threshold region is a range of voltages
for which the input voltage value cannot be interpreted reliably as either a 0 or a 1.

## Slide 21: Combination and Sequential Logic
Digital logic circuit can be classified into the following two categories:
  Combinational Logic: logic circuit without memory.
  Sequential Logic: logic circuit with memory.
We need both of combinational and sequential circuit to build computer system.
We will cover combinational logic the first.

## Slide 22: Basic Logic Gates (Functions)
AND Gate
  outputs 1 only if both inputs are 1
OR Gate
  outputs 1 if at least one input is 1
NOT Gate
  outputs 1 if input is 0 and outputs 0 if input is 1
A
B
AB
A
B
A+B
A
A’

## Slide 23: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT uses a switch
  such that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in series => AND
Switches in parallel => OR
C’
Normally-closed switch => NOT

## Slide 24: Summary
We finished our coverage on Chapter 1
We began to discuss our coverage on Digital logic gates and expression
We will have Quiz 1 on Friday, September 7