## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 5
September 5, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We discussed Integrated Circuit (IC) cost
Will continue to cover logic gates and expression today
Will learn:
  Logic gates and expression
  Boolean Equations
Homework #1 is due today at the beginning of the lecture (Hard Copy)
Key for HW 1 will post on Blackboard soon
We will have our first Quiz on Friday, Sept. 9, 2018, which will be on Lectures 1, 2, 3 and 4

## Slide 3: Basic Logic Gates (Functions)
AND Gate
  outputs 1 only if both inputs are 1
OR Gate
  outputs 1 if at least one input is 1
NOT Gate
  outputs 1 if input is 0 and outputs 0 if input is 1
A
B
AB
A
B
A+B
A
A’

## Slide 4: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT uses a switch
  such that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in series => AND
Switches in parallel => OR
C’
Normally-closed switch => NOT

## Slide 5: Logic Function Implementation (Continued)
Example: Logic Using Switches
Light is on (L = 1) for
  L(A, B, C, D) =
  and off (L = 0), otherwise.
Useful model for relay circuits and for CMOS gate circuits, the foundation of current digital logic technology
B
A
D
C’
Notes: L (A, B, C, D) = A ((B C') + D) = A B C' + A D

## Slide 6: True Table of Fundamental Logical Operations
Truth Table: standard table listing all possible combinations of inputs and resultant output for each. E.g.,
A | B | A  B | A + B | A’
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 7: Ludwig Wittgenstein (1889-1951)
Truth table method is proposed by philosopher Ludwig Wittgenstein in Tractatus (1922).
What we cannot speak about we must pass over in silence. - Ludwig Wittgenstein

## Slide 8: How to use Truth Table to Determine Digital Circuit Output?
A | B | C | BC | A+BC
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
C
B
BC
A
A+BC

## Slide 9: How to Design a Digital Circuit from Truth Table
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Output = AB’ + A’B
This function is called exclusive OR

## Slide 10: Truth Tables Exercise 1
A | B | C | A+B’C
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Complete the truth
table on the right.

## Slide 11: Truth Tables Exercise 2
A | B | C | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Draw the circuit to
implement the truth
table on the right.

## Slide 12: Boolean Equations
Boolean algebra is used to deal with logic equations. Boolean algebra can be used to simplify digital logic equations.
Boolean Operands
  Constants
    “1” and “0”
  Boolean variable
    Some identifier that can either be “1” or “0” at a given time
    The actual value is not known
Boolean Operators
  Combine Boolean values in different ways
  Can work with variables or constants
  Always result in a Boolean value
Boolean equation
  Combination of zero or more operators and operands