## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 7
September 10, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover fundamental combinational digital logic block
Will learn:
  More on logic gates
  Number Systems
  Fractional Number Systems
  We will begin to cover how to do math in the binary format and how to implement it in hardware
Quiz 1 grades and keys are posted on blackboard
  Mean: 6.83
  Variance: 3.71
  Median: 6
  Standard deviation: 1.93
Homework 1 grades are posted on blackboard as well
Homework 2 will post on blackboard soon

## Slide 3: Review: Laws of Boolean Algebra
Identity law
  A + 0 = A
  A1 = A
Zero and One laws
  A + 1 = 1
  A 0 = 0
Inverse laws
  A + A’ = 1
  A A’ = 0

## Slide 4: Review: Laws of Boolean Algebra Cont.
Commutative laws
  A + B = B + A
  A . B = B . A
Associative laws
  A + (B + C) = (A + B) + C
  (A . B) . C = A . (B . C)
Distributive laws
  A. (B + C) = (A.B) + (A.C)
  A+(B . C) = (A+B) . (A+C)

## Slide 5: Boolean Algebra: Additional Properties
Null elements
  a + 1 = 1
  a . 0 = 0
Idempotent Law
  a + a = a
  a .a = a
Involution Law
  (a’)’ = a
DeMorgan’s Law
  (a + b)’ = a’b’
  (ab)’ = a’ + b’
  Very useful!
To prove, just evaluate all possibilities

## Slide 6: Boolean Algebra Operator Precedence
High to low
  () – Inner most parentheses first
  NOT (’)
  AND ( •)
  OR (+)

## Slide 7: Example: how Boolean algebraic can simplify the logic expression
A + A·B = A (Absorption Theorem)
Proof Steps:
A + A·B
= A·1+A·B X = X · 1
= A·(1+B) X · Y + X · Z = X ·(Y +Z) (Distributive Law)
= A·1 1 + X = 1
= A X · 1 = X

## Slide 8: From Boolean Equations to Logic Circuits
Straightforward process
  Each operator becomes a Gate
  Suitably connect outputs to inputs
    Pay attention to crossing lines versus connected lines
  Label all inputs and outputs of each gate

## Slide 9: Example1: Example: Converting a Boolean Equation to a Circuit of Logic Gates
A.B.C.D
  (A.B).(C.D)
A
B
AB
C
D
CD
ABCD

## Slide 10: Example 2: Converting a Boolean Equation to a Circuit of Logic Gates
Q: Convert the following equation to logic gates: F = a AND NOT( b OR NOT(c) )
a
b
c
F
a
Start from the output, work back towards the inputs

## Slide 11: More examples
Start from the output, work back towards the inputs
a
s
d
F
(
a
)
F = a AND (s OR d)
1
2
a
a
a
b
c
F
(
b
)
F = (a AND NOT(b)) OR (b AND NOT(c))
2
1
3

## Slide 12: Using gates with more than 2 inputs
Can think of as AND(a,b,c)

## Slide 13: Multiple-Output Circuits
Many circuits have more than one output
Can give each a separate circuit, or can share gates
Ex: F = ab + c’, G = ab + bc
a
b
c
F
G
(
b
)
a
b
c
F
G
(
a
)
Option 1: Separate circuits
Option 2: Shared gates
a
a

## Slide 14: Other Common Logic Gates
(A+B)
NAND
NOR
Exclusive-OR (XOR)
A
B
(A.B)’
A
B
(A+B)’
A
B

## Slide 15: Exercises: Check for Yourself
Draw the logic circuit diagram for F=A+B’C.
Determine the truth table for the following logic equations: F=A’BC+A’BC’+AC.
Write the logic equation for the following circuit diagram
C
B
A
D
E

## Slide 16: Building Circuits Using Gates
Example
  Turn on lamp (F=1) when motion sensed (a=1) and no light (b=0)
  F = a AND NOT(b)
  Build using logic gates, AND and NOT, as shown
  We just built our first digital circuit!

## Slide 17: Summary
We discussed our coverage on digital logic with which we can built a very simple processor
We will start discussing number system next