## Slide 1: CSCIU 310 01 Introduction to Computer Architecture AKM Jahangir A Majumder, PhD
Spring 2019 - Lecture 4
January 28, 2019
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We began to cover how a datapath is built to implement MIPS instructions.
  We will discuss how to built a Control Signal Generation for data path
Please read the syllabus and sign on the acknowledgement sheet
HW 2 will post on Blackboard soon
We will have quiz 2 on Monday, January 4, which will cover Lectures 3-5
We will discuss feedback on proposal proposal next class

## Slide 3: Building the Datapath (for R-Type)
Example: addu $t0, $s1, $s2
Fetch Instruction
Read Two Registers
ALU Operation
Write Register
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 4: Building the Datapath (for Immediate)
Example: addi $t0, $s1, 100
Fetch Instruction
Read One Register
Signed extend immediate
Calculation Result
Read Data from Memory
Write Register
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 5: Building the Datapath (for Load/Store)
Example lw $s1, offset($s0)
Fetch Instruction
Read One Register ($s0)
Signed extend immediate (offset)
Calculation Address
Read Data from Memory
Write Register ($s1)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 6: Building the Datapath (Branch function)
Example: beq, $t1, $t2, offset
Fetch Instruction
Read Two Registers
ALU Operations
  ALU 1 perform Subtraction
  ALU 2 calculate PC+4+Offset
ALU Zero decide the next PC value
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 7: Review: The MIPS Instruction Formats
All MIPS instructions are 32 bits long. 3 formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation (“opcode”) of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
address/immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: One of the most important thing you need to know before you start designing a processor is how the instructions look like.
Or in more technical term, you need to know the instruction format. One good thing about the MIPS instruction set is that it is very simple.
First of all, all MIPS instructions are 32 bits long and there are only three instruction formats: (a) R-type, (b) I-type, and (c) J-type.
The different fields of the R-type instructions are:
(a) OP specifies the operation of the instruction.
(b) Rs, Rt, and Rd are the source and destination register specifiers.
(c) Shamt specifies the amount you need to shift for the shift instructions.
(d) Funct selects the variant of the operation specified in the “op” field.
For the I-type instruction, bits 0 to 15 are used as an immediate field. I will show you how this immediate field is used differently by different instructions.
Finally for the J-type instruction, bits 0 to 25 become the target address of the jump.
+3 = 10 min. (X:50)

## Slide 8: Control Signal
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
Example: add $t0, $s1, $s2 Instruction Format: 000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
ALU's operation based on instruction type and function code

## Slide 9: The Simple Datapath with Control Unit
Control Unit Output
  Branch
  MemRead
  MemtoReg
  ALUOp
  MemWrite
  ALUSrc
  RegWrite

## Slide 10: Review: The ALU Diagram
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
ALU 0~30
ALU 31

## Slide 11: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 12: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 13: ALU Control Signal Generation (1/2)
What should the ALU do with this instruction
Example: lw $1, 100($2) 35 2 1 100 op rs rt 16 bit offset
ALU control input 0000 AND 0001 OR 0010 add 0110 subtract 0111 set-on-less-than 1100 NOR

## Slide 14: ALU Control Signal Generation (2/2)
Must describe hardware to compute 4-bit ALU control input
  given instruction type 00 = lw, sw 01 = beq, 10 = arithmetic
  function code for arithmetic
Describe it using a truth table (can turn into gates):
ALUOp computed from instruction type

## Slide 15: How do the Datapath Implement a Beq Function?
X
0
01
1
0
0
0
X
0110

## Slide 16: How do the Processor Implement a beq Function (beq $t1, $t2, L)?
X
0
01
1
0
0
0
X
0110

## Slide 17: How do the Processor Implement an addu Function (addu $t1, $t2, $t3)?
0
0
0010
1
0
1
0
0

## Slide 18: How do the Processor Implement an sw Function (sw $t1 100($t2))?
1
1
0
0010
0
0
X
X

## Slide 19: Single Processor Control Signal Summary

## Slide 20: Review: J-Format Instructions (1/2)
Define “fields” of the following number of bits each:
6 bits
26 bits
opcode
target address
As usual, each field has a name:
Key Concepts
  Keep opcode field identical to R-format and I-format for consistency.
  Combine all other fields to make room for large target address.