## Slide 1: CSCIU 310 01 Introduction to Computer Architecture AKM Jahangir A Majumder, PhD
Spring 2019 - Lecture 5
January 30, 2019
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We began to cover how a datapath is built to implement MIPS instructions
We will also discuss the following topics:
  how the control signal can be generated in a processor
  issues of single cycle processor.
HW 2 is posted on Blackboard which is due on Wednesday, Feb 6
We will have quiz 2 on Monday, Feb 11, which will cover Lectures 3-5
Quiz 1 grades and keys are posted on Blackboard
We will discuss feedback on proposal proposal today

## Slide 3: Review: J-Format Instructions (1/2)
Define “fields” of the following number of bits each:
6 bits
26 bits
opcode
target address
As usual, each field has a name:
Key Concepts
  Keep opcode field identical to R-format and I-format for consistency.
  Combine all other fields to make room for large target address.

## Slide 4: Review: J-Format Instructions (2/2)
Summary:
  New PC = {PC[31..28], target address, 00}
Understand where each part came from!
Note: { , , } means concatenation {4 bits , 26 bits , 2 bits} = 32 bits address
  {1010, 11111111111111111111111111, 00} = 10101111111111111111111111111100
  Note: Book uses ||, Verilog uses { , , }

## Slide 5: Original Simple Datapath

## Slide 6: Extended Datapath for Jump Function Implementation
Note: Some Corrections has been made in the figure
1

## Slide 7: Control Signal Generation
Simple combinational logic (truth tables)

## Slide 9: Where we are headed
Single Cycle Problems:
  what if we had a more complicated instruction like floating point?
  wasteful of area
One Solution:
  use a “smaller” cycle time
  have different instructions take different numbers of cycles
  a “multicycle” datapath:

## Slide 10: Single Cycle Computer Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We can improve performance by pipelining

## Slide 11: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/0.5n + 1.5 ≈ 4 = number of stages