## Slide 1: CSCIU 310 01 Introduction to Computer Architecture AKM Jahangir A Majumder, PhD
Spring 2019 - Lecture 2
January 16, 2019
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will review materials covered in CSCI U 210 today
We will begin to cover how a datapath is built to implement MIPS instructions.
Please read the syllabus and sign on the acknowledgement sheet
We will have our first quiz on Monday, January 23 on MIPS assembly language
HW 2 will post on Blackboard soon
No Class on Monday, January 21 Dr. Martin Luther King day

## Slide 3
Review on CSCI U210 Syllabus

## Slide 4: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 5: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 6: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 7: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 8: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 9: Different Logic Gates
A
B
AB
A
B
A+B
A
A’
A
B
(A.B)’
A
B
(A+B)’
(A+B)
A
B
AND
OR
NOT
NAND
NOR
XOR
You need to memorize their symbols and functions

## Slide 10: Boolean Algebra and Truth Table
Boolean algebra can be used to describe binary logic.
Boolean algebra operators (in the order of priority):
  () : Parenthesis
  ‘ : NOT
   : AND
  + : OR
Truth table can be used to represent input-output relations of a digital system.
You should be able to derive a truth table for a given logic circuit or Boolean algebra presentation and vice versa.

## Slide 11: Example: Truth Table, Boolean Algebra, and Digital Logic Circuit
A | B | C | BC | A+BC
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
C
B
BC
A
A+BC

## Slide 12: Constructing Gates
It turns out that, because the way a transistor works, the easiest gates to create are the NOT, NAND, and NOR gates

## Slide 13: Laws of Boolean Algebra
Identity law
  A + 0 = A
  A1 = A
Zero and One laws
  A + 1 = 1
  A 0 = 0
Inverse laws
  A + A’ = 1
  A A’ = 0
Commutative laws
  A + B = B + A
  A . B = B . A
Associative laws
  A + (B + C) = (A + B) + C
  A . (B . C) = A . (B . C)
Distributive laws
  A. (B + C) = (A.B) + (B.C)
  A+(B . C) = (A+B) . (A+C)
DeMorgan’s laws
  (AB)’=A’+B’
  (A+B)’=A’ B’

## Slide 14: Binary Math: Base Conversion
In everyday life, we used decimal base system which uses 10 as base.
In computer systems, binary base and other related bases such as hexadecimal base are used.
Example:
  3.2510 =11.012
  CF.116=11001111.00012
Note: In your exam, any conversion problem answer in format of M/N will receive no credit.

## Slide 15: Binary Numbers
Some terminology and units
  Bit (b): A single binary digit
  Nib: 4 bits
  Byte (B): 8-bits
  Word: A group of bits of any size (often 4 bytes).
  kb: 210 bits = 1024 bits (kB = 210 bytes)
  Mb: 220 bits =1,048,576 bits (MB = 220 bytes)
  Gb: 230 bits = 1,073,741,820 bits (GB = 230 bytes)
  MSB: Most significant bit (leftmost digit of binary #)
  LSB: Least significant bit (rightmost digit of bin. #)

## Slide 16: Binary to Decimal Conversion
···b3b2b1b0 (each bit bi is 0 or 1)
b0×20 + b1×21 + b2×22 + b3×23 + ···
= b0×1 + b1×2 + b2×4 + b3×8 + ···
Binary Number:
Its decimal value is:
Examples: 11102 Decimal value is:
11112 Decimal value is:
1100102 Decimal value is:
1111112 Decimal value is:
Check your understanding:
N bits  2N combinations  decimal numbers 0, 1, 2, 3, …, 2N - 1
The largest number: 11…112 = 2N-1 (decimal)
14
15
50
63
N bits, all ones

## Slide 17: Other Conversions
Convert decimal to hex
Use the successive division method described previously (for decimal to binary), but divide by 16 instead of 2.
Convert binary to hex
  A hex digit is equivalent to 4 bits.
  Divide binary number into groups of 4 bits, starting from the right.
  Convert each 4 bit group into one hex digit.
Convert hex to binary
  Convert each hex digit to its 4-bit binary equivalent.
  String the bits together.
Note: Computationally, it’s easy to convert between bases that are powers of 2, as indicated in the binary to hex conversion technique above.

## Slide 18: Other Conversions
Convert decimal to Octal
Use the successive division method described previously (for decimal to binary), but divide by 8 instead of 2.
Convert binary to Octal
  A octal digit is equivalent to 3 bits.
  Divide binary number into groups of 3 bits, starting from the right.
  Convert each 3 bit group into one octal digit.
Convert octal to binary
  Convert each octal digit to its 3-bit binary equivalent.
  String the bits together.
(examples on next slide)

## Slide 19: Fractions
Binary number: 0.b-1b-2b-3b-4···
Decimal value: b-1×2-1 + b-2×2-2 + b-3×2-3 + b-4×2-4 + ···
Binary to Decimal Conversion
Decimal to Binary Conversion: Successive multiplication by 2
Example: Decimal number 0.6875
Example: 0.1012 = 1×2-1 + 0×2-2 + 1×2-3 = 0.62510
0.68752 = 1.375  b-1 = 1 and 1.375-1 = 0.375
0.3752 = 0.75  b-2 = 0 and 0.75-0 = 0.75
0.752 = 1.5  b-3=1 and 1.5-1 = 0.5
0.52 = 1  b-4=1 and 1-1 = 0
Binary representation: 0.1011

## Slide 20: 1 Bit Full Adder Implementation
cin
b
a
s
Å
Å
=
cin
)
b
a
(
b
a
cout
Å
+
=
a
b
carry in
carry out
sum

## Slide 21: Binary Math: 2’s Complement
In binary world, people use 2’s complement to represent signed integer and implement subtraction.
The procedure of getting 2’s complement of a given number:
  Invert every bit
  Then add 1
For n bit signed integer, its representation is -2n-1 ~ 2n-1-1
  Example
    110011002 = - (00110100)2 = -5210
    100000002 = -12810

## Slide 22: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 23: Binary Math: Overflow Detection
Overflow happens when the calculation result is beyond the representation range for given number of bits.
Overflow might happen in one of following situations:
  Positive + Positive
  Negative + Negative
  Positive – Negative
  Negative – Positive
Important: You should determine whether an overflow happen by checking sign bits.
Example:
  Overflow: 11000000+10000000=01000000 (the extra carry out bit is discarded)
  Overflow: 01000000+01000000=10000000 (no extra bit)
  No Overflow 01000000+11000000=00000000 (the extra carry out bit is discarded)

## Slide 24: Multiplication and Division by Shifting Bits
We will cover multiplication in great details later. However, some simple multiplication can be accomplished simply by shifting the bit sequence.

## Slide 25: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000

## Slide 26: Shifting and Multiplication
Shift Left a binary number by i bits will give the same result as multiplying by 2i. (True or False)
Shift Right a binary number by i bits will give the same result as dividing by 2i. (True or False)

## Slide 27: Decoder
Popular combinational logic building block, in addition to logic gates
Collection of logic gates which are arranged in a specific way that converts input binary number to one high output
2-input decoder: four possible input binary numbers... So has four outputs, one for each possible input binary number

## Slide 28: Building of 4-to-1-line Multiplexer
2-to-22-line decoder
22 ´ 2 AND-OR

## Slide 29: The ALU Diagram
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
ALU 0~30
ALU 31
Can this ALU implement a NAND function?

## Slide 30: Introduction to Sequential Circuits
A Sequential circuit contains:
  Storage elements: Latches or Flip-Flops
  Combinatorial Logic:
    Implements a multiple-output switching function
    Inputs are signals from the outside.
    Outputs are signals to the outside.
    Other inputs, State or Present State, are signals from storage elements.
    The remaining outputs, Next State are inputs to storage elements.
Combina-tional
Logic
Storage Elements
Inputs
Outputs
State
Next
State

## Slide 31: The Latch Timing Problem (continued)
Consider the following circuit:
Suppose that initially Y = 0.
As long as C = 1, the value of Y continues to change!
The changes are based on the delay present on the loop through the connection from Y back to Y.
This behavior is clearly unacceptable.
Desired behavior: Y changes only once per clock pulse
Clock
Y
C
D
Q
Q
Y
Clock

## Slide 32: Storage Element’s Timing Model
Setup Time: Input must be stable BEFORE trigger clock edge
Hold Time: Input must REMAIN stable after trigger clock edge
Clock-to-Q time:
  Output cannot change instantaneously at the trigger clock edge
  Similar to delay in logic gates, two components:
    Internal Clock-to-Q
    Load dependent Clock-to-Q
Typical for class: 1ns Setup, 0.5ns Hold
D
Q
D
Don’t Care
Don’t Care
Clk
Unknown
Q
Setup
Hold
Clock-to-Q
Notes: So far we have been looking at combinational logic, let’s look at the timing characteristic of a storage element.
The storage element you will use is a D type flip-flop trigger on the negative clock edge.
In order for the data to latch into the flip flop correctly, the input must be stable slightly before the falling edge of the clock. This time is called the Setup time.
After the clock edge has arrived, the data must remain stable for a short amount of time AFTER the trigger clock edge. This is called the hold time.
The output cannot change instantaneously at the trigger clock edge. The time it takes for the output to change to its new value after the clock is called the Clock-to-Q time.
Similar to delay in logic gates, the Clock-to-Q time has two components:
(a) The internal Clock-to-Q time: the time it takes the output to change if output load is zero.
(b) And the load dependent Clock-to-Q time.
+2 = 50 min. (Y:30)

## Slide 33: Machine Format
Our processor’s machine code format is given below
  [load, regad1, regad2, des_regad, aluop]
    load signal: 1 (read from external input), 0 (read from ALU)
    regad1: the address of the register for the ALU input 1
    regad2: the address of the register for the ALU input 2
    des_regad: the address of the destination register which data is written into
    aluop: the ALU function selection
There are 16 registers and 8 ALU functions.
Question: Based on the above description of the processor, how many bits each command should have?

## Slide 34: MIPS Assembly Language
We’ll be working with the MIPS instruction set architecture
  developed in 1985
  means “Microprocessor without Interlocked Pipeline Stages”
  similar to other architectures developed since the 1980's
  almost 100 million MIPS processors manufactured in 2002
  used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, …
  a Reduced Instruction Set Computer (RISC) Assembly Language
Instruction Category:
  Arithmetic: Add, Subtract,…
  Data Transfer: Load Word,…
  Logical: And, Or,…
  Conditional Branch: Branch on Equal,…
  Unconditional Jump: Jump

## Slide 35: MIPS Computer Simulator: SPIM
SPIM is a simulator developed for MIPS computer simulation.
You can download SPIM simulator PCSpim http://www.cs.wisc.edu/~larus/spim.html

## Slide 36: Assembly Variables: Registers Cont..
Registers are numbered from 0 to 31
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31

## Slide 37: Assembly Variables: Registers Cont…
By convention, each register also has a name to make it easier to code
For now:
  $16 - $23  $s0 - $s7
  (correspond to C variables)
  $8 - $15  $t0 - $t7
  (correspond to temporary variables)
In general, use names to make your code more readable

## Slide 38: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, the registers have no type; operation determines how register contents are treated

## Slide 39: MIPS Registers
USE Number Name
The constant 0 $0 $zero
Reserved for Assembler $1 $at
Return Values $2-$3 $v0-$v1
Arguments $4-$7 $a0-$a3
Temporary $8-$15 $t0-$t7
Saved Temporaries $16-$23 $s0-$s7
Temporary $24-$25 $t8-$t9
Used by Kernel $26-$27 $k0-$k1
Global Pointer $28 $gp
Stack Pointer $29 $sp
Frame Pointer $30 $fp
Return Address $31 $ra

## Slide 40: Registers vs. Memory
Arithmetic instructions operands must be registers, — only 32 registers provided
Which computer components do registers belongs to?
Compiler associates variables with registers
What about programs with lots of variables?
Processor
I/O
Control
Datapath
Memory
Input
Output

## Slide 41: Comments in MIPS Programs
You can use comments to make your code more readable.
Hash (#) is used for MIPS comments
  anything from hash mark to end of line is a comment and will be ignored
Note: Different from C.
  C comments have format /* comment */ so they can span many lines

## Slide 42: MIPS Addition and Subtraction (1/4)
Syntax of Instructions:
  1 2, 3, 4
  where:
  1) operation by name
  2) operand getting result (“destination”)
  3) 1st operand for operation (“source1”)
  4) 2nd operand for operation (“source2”)
Syntax is rigid:
  1 operator, 3 operands
  Operand order is fixed (destination first)
  Why? Keep Hardware simple via regularity
Design Principle: simplicity favors regularity.

## Slide 43: Addition and Subtraction of Integers (2/4)
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where MIPS registers $s0,$s1,$s2 are associated with C variables a, b, c
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where MIPS registers $s3,$s4,$s5 are associated with C variables d, e, f

## Slide 44: Addition and Subtraction of Integers (3/4)
How do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
Notice: A single line of C may break up into several lines of MIPS.
Notice: Everything after the hash mark on each line is ignored (comments)

## Slide 45: Addition and Subtraction of Integers (4/4)
How do we do this?
f = (g + h) - (i + j);
Use intermediate temporary register
  add $t0,$s1,$s2 # temp = g + h
  add $t1,$s3,$s4 # temp = i + j
  sub $s0,$t0,$t1 # f=(g+h)-(i+j)

## Slide 46: Immediates
Immediates are numerical constants.
They appear often in code, so there are special instructions for them.
Add Immediate:
  addi $s0,$s1,10 (in MIPS)
  f = g + 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
Syntax similar to add instruction, except that last argument is a number instead of a register.

## Slide 47: Immediates
There is no Subtract Immediate in MIPS:
Limit types of operations that can be done to absolute minimum
  if an operation can be decomposed into a simpler operation, don’t include it
  addi …, -X = subi …, X => so no subi
addi $s0,$s1,-10 (in MIPS)
  f = g - 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g

## Slide 48: Register Zero
One particular immediate, the number zero (0), appears very often in code.
So we define register zero ($0 or $zero) to always have the value 0; eg
  add $s0,$s1,$zero (in MIPS)
  f = g (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
defined in hardware, so an instruction
  add $zero,$zero,$s0
will not do anything!

## Slide 49: Review: MIPS Instruction Format
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide

## Slide 50: Machine Language: R-Type
Numeric version of instructions is called machine language
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers, $t0=8, $s1=17, $s2=18
Instruction Format: add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
Can you guess what the field names stand for?
Notes: Board work: Binary Numbers

## Slide 51: Machine Language: I-Type
Consider the addi instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for immediates
  other format was R-type for register
Example: addi $s1, $s2, 100 8 18 17 100 op rs rt 16 bit number

## Slide 52: MIPS Fields
op: Basic operation of the instruction, opcode
rs: The first register source operand
rt: The second register source operand
rd: The register destination operand.
shamt: Shift amount
funct: Function

## Slide 53: Assembly Operands: Memory
C variables map onto registers; what about large data structures like arrays?
1 of 5 components of a computer: memory contains such data structures
But MIPS arithmetic instructions only operate on registers, never directly on memory.
Data transfer instructions transfer data between registers and memory:
  Memory to register
  Register to memory

## Slide 54: Anatomy: 5 components of any Computer
Personal Computer
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
Load (from)
Store (to)
These are “data transfer” instructions…
Registers are in the datapath of the processor; if operands are in memory, we must transfer them to the processor to operate on them, and then transfer back to memory when done.
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 55: Data Transfer: Memory to Reg (1/4)
To transfer a word of data, we need to specify two things:
  Register: specify this by # ($0 - $31) or symbolic name ($s0,…, $t0, …)
  Memory address: more difficult
    Think of memory as a single one-dimensional array, so we can address it simply by supplying a pointer to a memory address.
    Other times, we want to be able to offset from this pointer.
Remember: “Load FROM memory”

## Slide 56: Data Transfer: Memory to Reg (2/4)
To specify a memory address to copy from, specify two things:
  A register containing a pointer to memory
  A numerical offset (in bytes)
The desired memory address is the sum of these two values.
Example: 8($t0)
  specifies the memory address pointed to by the value in $t0, plus 8 bytes

## Slide 57: Data Transfer: Memory to Reg (3/4)
Load Instruction Syntax:
  1 2, 3(4)
  where
  1) operation name
  2) register that will receive value
  3) numerical offset in bytes
  4) register containing pointer to memory
MIPS Instruction Name:
  lw (meaning Load Word, so 32 bits or one word are loaded at a time)

## Slide 58: Data Transfer: Memory to Reg (4/4)
Example: lw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then load the value from the memory pointed to by this calculated sum into register $t0
Notes:
  $s0 is called the base register
  12 is called the offset
  offset is generally used in accessing elements of array or structure: base reg points to beginning of array or structure
Data flow

## Slide 59: Data Transfer: Reg to Memory
Also want to store from register into memory
  Store instruction syntax is identical to Load’s
MIPS Instruction Name:
sw (meaning Store Word, so 32 bits or one word are loaded at a time)
Example: sw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then store the value from register $t0 into that memory address
Remember: “Store INTO memory”
Data flow

## Slide 60: System Calls
SPIM provides a small set of operating-system-like services through the system call (syscall) instruction.
To request a service, a program load the system call code into the register $v0 and arguments into registers $a0-$a3.

## Slide 61: Pseudoinstruction
The following two instructions are not real MIPS instruction. They can be implemented with real MIPS instruction though. Therefore, they are called “pseudoinstructions.” They are created for the convenience of programmers.
li $reg, imm (load immediate)
  - $reg=imm
la $reg address (load address)
  - $reg=address
To use pseudoinstructions, you need to specify that pseudoinstrcutions is allowed in the setting of SPIM simulator.

## Slide 62: Assembler Directives
Assembler directives begin a period.
Assembler directives tell the assembler how to translate a program but do not produce machine code for itself.
Example:
  .globl sym: declare that label sym is global and can be referred from other files.
  .text: subsequent items are put in the user segment. In SPIM, these items may only be instructions or words.
  .data: declare that subsequent items are stored in the data segment.
  .asciiz str: store the string str in memory and null-terminated

## Slide 63: The First Program: Hello World
.text
.globl main
main:
li $v0, 4
la $a0, str
syscall # print string
li $v0, 10
syscall # exit (you must use syscall #10 to exit)
.data
str: .asciiz "Hello World!!!"

## Slide 64: MIPS Data Transfer Instructions Example
C code: A[12] = h + A[8]; MIPS code: lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
$s3: base address (as called index register)
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory! Can’t write: add 48($s3), $s2, 32($s3)
Word Address
Byte Address

## Slide 65: Pointers v. Values
Key Concept: A register can hold any 32-bit value. That value can be a (signed) int, an unsigned int, a pointer (memory address), and so on
If you write add $t2,$t1,$t0 then $t0 and $t1 better contain values
If you write lw $t2,0($t0) then $t0 better contain a pointer
Don’t mix these up!

## Slide 66: Addressing: Byte vs. Word
Every word in memory has an address, similar to an index in an array
Early computers numbered words like C numbers elements of an array:
  Memory[0], Memory[1], Memory[2], …
Called the “address” of a word
Computers needed to access 8-bit bytes as well as words (4 bytes/word)
Today machines address memory as bytes, (i.e.,“Byte Addressed”) hence 32-bit (4 byte) word addresses differ by 4
  Memory[0], Memory[4], Memory[8], …

## Slide 67: Compilation with Memory
What offset in lw to select A[5] in C?
4x5=20 to select A[5]: byte v. word
Compile by hand using registers: g = h + A[5];
  g: $s1, h: $s2, $s3:base address of A
1st transfer from memory to register:
lw $t0,20($s3) # $t0 gets A[5]
  Add 20 to $s3 to select A[5], put into $t0
Next add it to h and place in g add $s1,$s2,$t0 # $s1 = h+A[5]

## Slide 68: Notes about Memory
Pitfall: Forgetting that sequential word addresses in machines with byte addressing do not differ by 1.
  Many an assembly language programmer has toiled over errors made by assuming that the address of the next word can be found by incrementing the address in a register by 1 instead of by the word size in bytes.
  So remember that for both lw and sw, the sum of the base address and the offset must be a multiple of 4 (to be word aligned)

## Slide 69: More Notes about Memory: Alignment
MIPS requires that all words start at byte addresses that are multiples of 4 bytes
0 1 2 3
Aligned
Not
Aligned
Called Alignment: objects must fall on address that is multiple of their size.
0, 4, 8, or Chex
Last hex digit of address is:
1, 5, 9, or Dhex
2, 6, A, or Ehex
3, 7, B, or Fhex

## Slide 70: MIPS Control Instruction I: Conditional Branch
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions:
bne $t0, $t1, Label : if ($t0!=$t1) go to Label beq $t0, $t1, Label : if ($t0==$t1) go to Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....

## Slide 71: MIPS Control Instruction II: Unconditional Jump
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Technically, it’s the same as:
  beq $0,$0,label
  since it always satisfies the condition.

## Slide 72: Example: Compiling C if into MIPS (1/2)
Compile by hand
  if (i == j) f=g+h; else f=g-h;
Use this mapping: f: $s0 g: $s1 h: $s2 i: $s3 j: $s4
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j

## Slide 73: Example: Compiling C if into MIPS (2/2)
Final compiled MIPS code:
beq $s3,$s4,True # branch i==j sub $s0,$s1,$s2 # f=g-h(false) j Fin # goto Fin True: add $s0,$s1,$s2 # f=g+h (true) Fin:
Note: Compiler automatically creates labels to handle decisions (branches). Generally not found in HLL code.
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j
Compile by hand
  if (i == j) f=g+h; else f=g-h;

## Slide 74: Inequalities in MIPS (1/5)
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Create a MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning: reg1 = (reg2 < reg3);
  if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  Usually, “set” means “set to 1”, “reset” means “set to 0”.
Same thing…

## Slide 75: Inequalities in MIPS (2/5)
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$0,Less # goto Less # if $t0!=0 # (if (g<h)) Less:
Branch if $t0 != 0  (g < h)
Register $0 always contains the value 0, so bne and beq often use it for comparison after an slt instruction.
A slt  bne pair means if(… < …)goto…

## Slide 76: Inequalities in MIPS (3/5)
We covered two pseudo instructions, li and la, in our SPIM tutorial session.
The following pseudo instruction is also useful:
"blt $s1, $s2, Label“
    called “branch on less than”
    can now build general control structures
Note that the assembler needs a register ($at: assembler temporary) to do this,
  there are policy of use conventions for registers
Notes: Board work: Binary Numbers

## Slide 77: Inequalities in MIPS (4/5)
Now, we can implement <, but how do we implement >, ≤ and ≥ ?
We could add 3 more instructions, but:
  MIPS goal: Simpler is Better
Can we implement ≤ in one or more instructions using just slt and the branches?
What about >?
What about ≥?

## Slide 78: Inequalities in MIPS (5/5)
if (g >= h) goto Loop #g:$s0, h:$s1
Loop: . . .
slt $t0,$s0,$s1 # $t0 = 1 if # $s0<$s1 (g<h) beq $t0,$0,Loop # goto Loop # if $t0==0 # if (g  h))
C
M I P S
A slt  beq pair means if(… ≥ …)goto…

## Slide 79: Example: The C Switch Statement (1/3)
Choose among four alternatives depending on whether k has the value 0, 1, 2 or 3. Compile this C code: switch (k) { case 0: f=i+j; break; /* k=0 */ case 1: f=g+h; break; /* k=1 */ case 2: f=g–h; break; /* k=2 */ case 3: f=i–j; break; /* k=3 */ }

## Slide 80: Example: The C Switch Statement (2/3)
This is complicated, so simplify.
Rewrite it as a chain of if-else statements, which we already know how to compile:
  if(k==0) f=i+j; else if(k==1) f=g+h; else if(k==2) f=g–h; else if(k==3) f=i–j;
Use this mapping:
  f:$s0, g:$s1, h:$s2, i:$s3, j:$s4, k:$s5

## Slide 81: Example: The C Switch Statement (3/3)
Final compiled MIPS code: bne $s5,$0,L1 # branch k!=0 add $s0,$s3,$s4 #k==0 so f=i+j j Exit # end of case so Exit L1: addi $t0,$s5,-1 # $t0=k-1 bne $t0,$0,L2 # branch k!=1 add $s0,$s1,$s2 #k==1 so f=g+h j Exit # end of case so Exit L2: addi $t0,$s5,-2 # $t0=k-2 bne $t0,$0,L3 # branch k!=2 sub $s0,$s1,$s2 #k==2 so f=g-h j Exit # end of case so Exit L3: addi $t0,$s5,-3 # $t0=k-3 bne $t0,$0,Exit # branch k!=3 sub $s0,$s3,$s4 #k==3 so f=i-j Exit:

## Slide 82: MIPS Control Instructions Syntax
Instruction Meaning bne $s4,$s5,L Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label slt $s1,$s2,$s3 if ($s2<$s3) $s1=1; else $s1=0
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 83: MIPS Logical Operations
Three basic logical operators in MIPS:
  AND: outputs 1 only if both inputs are 1
  OR: outputs 1 if at least one input is 1
  NOR: outputs 1 if both inputs are 0
Truth Table: standard table listing all possible combinations of inputs and resultant output for each. E.g.,
A | B | A AND B | A OR B | A NOR B
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 84: Logical Instruction Syntax
R-Format
op rs rt rd shamt funct
I-Format
op rs rt 16 bit number
  $s1 = $s2&$s3: and $s1, $s2, $s3
  $s1 = $s2|$3: or $s1, $s2, $s3
  $s1 = ~($s2|$s3): nor $s1, $s2, $s3
There is another important logical function, NOT.
NOT (1) = 0 and NOT (0) = 1.
How to implement NOT function (~) with MIPS instruction?

## Slide 85: Exercise: Implement NOT function with NOR instruction
A NOR 0 = NOT (A)
Nor $s1, $s2, $zero : $s1=~$s2

## Slide 86: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000
  What arithmetic effect does shift left have?

## Slide 87: Shift Instruction Syntax
MIPS shift instructions:
1. sll (shift left logical): shifts left and fills emptied bits with 0s
2. srl (shift right logical): shifts right and fills emptied bits with 0s
Machine version of “sll $t2, $s0, 4”:
op rs rt rd shamt funct
0 0 16 10 4 0

## Slide 88: Loops in C/Assembly (1/3)
Simple loop in C; A[] is an array of integers
  do {g = g + A[i];
  i = i + j; } while (i != h);
Rewrite this as:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5

## Slide 89: Loops in C/Assembly (2/3)
Final compiled MIPS code:
Loop: sll $t1,$s3,2 #$t1= 4*i add $t1,$t1,$s5 #$t1=addr A lw $t1,0($t1) #$t1=A[i] add $s1,$s1,$t1 #g=g+A[i] add $s3,$s3,$s4 #i=i+j bne $s3,$s2,Loop# goto Loop # if i!=h
Original code:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5
Notes: Do goto first
Then I = I + J
Then 1st 4

## Slide 90: Example: The C Switch Statement (2/3)
This is complicated, so simplify.
Rewrite it as a chain of if-else statements, which we already know how to compile:
  if(k==0) f=i+j; else if(k==1) f=g+h; else if(k==2) f=g–h; else if(k==3) f=i–j;
Use this mapping:
  f:$s0, g:$s1, h:$s2, i:$s3, j:$s4, k:$s5

## Slide 91: Example: The C Switch Statement (3/3)
Final compiled MIPS code: bne $s5,$0,L1 # branch k!=0 add $s0,$s3,$s4 #k==0 so f=i+j j Exit # end of case so Exit L1: addi $t0,$s5,-1 # $t0=k-1 bne $t0,$0,L2 # branch k!=1 add $s0,$s1,$s2 #k==1 so f=g+h j Exit # end of case so Exit L2: addi $t0,$s5,-2 # $t0=k-2 bne $t0,$0,L3 # branch k!=2 sub $s0,$s1,$s2 #k==2 so f=g-h j Exit # end of case so Exit L3: addi $t0,$s5,-3 # $t0=k-3 bne $t0,$0,Exit # branch k!=3 sub $s0,$s3,$s4 #k==3 so f=i-j Exit:

## Slide 92: MIPS Control Instructions Syntax
Instruction Meaning bne $s4,$s5,L Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label slt $s1,$s2,$s3 if ($s2<$s3) $s1=1; else $s1=0
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 93: MIPS R3000 Instruction Set Architecture (Summary)
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
Registers

## Slide 94: Review: MIPS Fields
op: Basic operation of the instruction, opcode
rs: The first register source operand
rt: The second register source operand
rd: The register destination operand.
shamt: Shift amount
funct: Function

## Slide 95: MIPS Logical Operations
Three basic logical operators in MIPS:
  AND: outputs 1 only if both inputs are 1
  OR: outputs 1 if at least one input is 1
  NOR: outputs 1 if both inputs are 0
Truth Table: standard table listing all possible combinations of inputs and resultant output for each. E.g.,
A | B | A AND B | A OR B | A NOR B
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 96: Logical Instruction Syntax
R-Format
op rs rt rd shamt funct
I-Format
op rs rt 16 bit number
  $s1 = $s2&$s3: and $s1, $s2, $s3
  $s1 = $s2|$3: or $s1, $s2, $s3
  $s1 = ~($s2|$s3): nor $s1, $s2, $s3
There is another important logical function, NOT.
NOT (1) = 0 and NOT (0) = 1.
How to implement NOT function (~) with MIPS instruction?

## Slide 97: Exercise: Implement NOT function with NOR instruction
A NOR 0 = NOT (A)
Nor $s1, $s2, $zero : $s1=~$s2

## Slide 98: Exercise
$s2: 1011 0110 1010 0100 0011 1101 1001 1010
$s3: 0000 0000 0000 0000 0000 1111 0000 0000
and $s1, $s2, $s3
$s1=?

## Slide 99: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000
  What arithmetic effect does shift left have?

## Slide 100: Shift Instruction Syntax
MIPS shift instructions:
1. sll (shift left logical): shifts left and fills emptied bits with 0s
2. srl (shift right logical): shifts right and fills emptied bits with 0s
Machine version of “sll $t2, $s0, 4”:
op rs rt rd shamt funct
0 0 16 10 4 0

## Slide 101: Exercise: Shift Operations
Let $S0= 0001 0010 0011 0100 0101 0110 0111 1000
sll $t2, $s0, 4
$t2 = ?
srl $t2, $s0, 8
$t2 = ?

## Slide 102: Loops in C/Assembly (1/3)
Simple loop in C; A[] is an array of integers
  do {g = g + A[i];
  i = i + j; } while (i != h);
We can rewrite this as:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5

## Slide 103: Loops in C/Assembly (2/3)
Final compiled MIPS code:
Loop: sll $t1,$s3,2 #$t1= 4*i add $t1,$t1,$s5 #$t1=addr A lw $t1,0($t1) #$t1=A[i] add $s1,$s1,$t1 #g=g+A[i] add $s3,$s3,$s4 #i=i+j bne $s3,$s2,Loop# goto Loop # if i!=h
Original code:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, base of A $s1, $s2, $s3, $s4, $s5
Notes: Do goto first
Then I = I + J
Then 1st 4

## Slide 104: Loops in C/Assembly (3/3)
There are three types of loops in C:
  while
  do… while
  for
Each can be rewritten as either of the other two, so the method used in the previous example can be applied to while and for loops as well.
Key Concept: Though there are multiple ways of writing a loop in MIPS, the key to decision making is conditional branch

## Slide 105: Partial SPIM System Service List
  print_int $a0=integer
  print_float $f12=float
  print_double $f12=double
  print_string $a0=string
  read_int put integer in $v0
  read_float put float number in $fo
  read_double put double in $fo
  read_string $a0=buffer, $a1=length
  sbrk address in $vo
  exit

## Slide 106: Constants
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
Solutions? Why not?
  put 'typical constants' in memory and load them.
  create hard-wired registers (like $zero) for constants like one.
MIPS Instructions: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
Design Principle: Make the common case fast. Which format?

## Slide 107: How about larger constants?
We'd like to be able to load a 32 bit constant into a register
Must use two instructions, new "load upper immediate" instruction lui $t0, 1010101010101010
Then must get the lower order bits right, i.e., ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
0000000000000000
1010101010101010
1010101010101010
1010101010101010
ori
1010101010101010
0000000000000000
filled with zeros

## Slide 108: Overflow in Arithmetic (1/2)
Reminder: Overflow occurs when there is a mistake in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  +15 1111
  +3 0011
  +18 10010
  But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and wrong.

## Slide 109: Overflow in Arithmetic (2/2)
Some languages detect overflow (Ada), some don’t (C)
MIPS solution is 2 kinds of arithmetic instructions to recognize 2 choices:
  add (add), add immediate (addi) and subtract (sub) cause overflow to be detected
  add unsigned (addu), add immediate unsigned (addiu) and subtract unsigned (subu) do not cause overflow detection
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 110: Immediates in Inequalities
There is also an immediate version of slt to test against constants: slti
  Helpful in for loops
if (g >= 1) goto Loop
Loop: . . . slti $t0,$s0,1 # $t0 = 1 if # $s0<1 (g<1) beq $t0,$0,Loop # goto Loop # if $t0==0 # (if (g>=1))
C
M I P S
A slt  beq pair means if(… ≥ …)goto…

## Slide 111: What about unsigned numbers?
Also unsigned inequality instructions:
sltu, sltiu
…which sets result to 1 or 0 depending on unsigned comparisons
What is value of $t0, $t1?
($s0 = FFFF FFFAhex, $s1 = 0000 FFFAhex)
slt $t0, $s0, $s1
sltu $t1, $s0, $s1

## Slide 112: Loading, Storing bytes (1/2)
In addition to word data transfers (lw, sw), MIPS has byte data transfers:
load byte: lb: load a byte from the memory, placing it in the rightmost 8 bits of a register.
store byte: sb: take a byte from the rightmost 8 bits of a register and write it to the memory.
same format as lw, sw

## Slide 113: Loading, Storing bytes (2/2)
x
What do with other 24 bits in the 32 bit register?
  lb: sign extends to fill upper 24 bits
byte loaded
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
zzz zzzz
Normally don't want to sign extend chars
MIPS instruction that doesn’t sign extend when loading bytes:
load byte unsigned: lbu

## Slide 114: MIPS Signed vs. Unsigned – different meanings!
MIPS Signed v. Unsigned is an “overloaded” term
  Do/Don't sign extend (lb, lbu)
  Don't overflow (addu, addiu, subu, multu, divu)
  Do signed/unsigned compare (slt, slti/sltu, sltiu)

## Slide 115: Procedure in C functions
main() { int i,j,k,m; ... i = mult(j,k); ... m = mult(i,i); ...
}
/* really dumb mult function */
int mult (int mcand, int mlier){ int product;
product = 0; while (mlier > 0) { product = product + mcand; mlier = mlier -1; } return product; }
What information must compiler/programmer keep track of?
What instructions can
accomplish this?

## Slide 116: Function Call Bookkeeping
Registers play a major role in keeping track of information for function calls.
Register conventions:
  Return address $ra
  Arguments $a0, $a1, $a2, $a3
  Return value $v0, $v1
  Local variables $s0, $s1, … , $s7
The stack is also used; more later.

## Slide 117: Instruction Support for Functions (1/6)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address 1000 1004 1008 1012 1016
2000 2004
C
M I P S
In MIPS, all instructions are 4 bytes, and stored in memory just like data. So here we show the addresses of where the programs are stored.

## Slide 118: Instruction Support for Functions (2/6)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address 1000 add $a0,$s0,$zero # x = a 1004 add $a1,$s1,$zero # y = b 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #jump to sum 1016 ...
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S

## Slide 119: Instruction Support for Functions (3/6)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S
Question: Why use jr here? Why not simply use j?
Answer: sum might be called by many functions, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.

## Slide 120: Instruction Support for Functions (4/6)
Single instruction to jump and save return address: jump and link (jal)
Before: 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #goto sum
After: 1008 jal sum # $ra=1012,goto sum
Why have a jal? Make the common case fast: function calls are very common. Also, you don’t have to know where the code is loaded into memory with jal.

## Slide 121: Instruction Support for Functions (5/6)
Syntax for jal (jump and link) is same as for j (jump):
  jal label
jal should really be called laj for “link and jump”:
  Step 1 (link): Save address of next instruction into $ra (Why next instruction? Why not current one?) – infinite loop
  Step 2 (jump): Jump to the given label

## Slide 122: Instruction Support for Functions (6/6)
Syntax for jr (jump register):
  jr register
Instead of providing a label to jump to, the jr instruction provides a register which contains an address to jump to.
Only useful if we know exact address to jump to.
Very useful for function calls:
  jal stores return address in register ($ra)
  jr $ra jumps back to that address

## Slide 123: Stored Program Concept
Instructions are bits
Programs are stored in memory — to be read or written just like data
Fetch & Execute Cycle
  Instructions are fetched and put into a special register
  Bits in the register "control" the subsequent actions
  Fetch the “next” instruction and continue
Processor
Memory
memory for data, programs,
compilers, editors, etc.

## Slide 124: A MIPS Computer Architecture

## Slide 125: MIPS Register and Instructions to Implement Procedure
Register Name Meaning
PC Program Counter (hold the address of the current instruction)
$ra return address
Instruction Name Example Meaning
Jump-and-link: jal L $ra=PC+4; go to L
Jump register: jr $ra go to $ra

## Slide 126: Procedure of Calling Function
jal
jr $ra
PC
PC
PC
PC
PC
PC+4->$ra

## Slide 127: MIPS Register Conventions
Note: Register 1 ($at) reserved for assembler, 26-27 for operating system

## Slide 128: Nested Procedures (1/2)
Procedure that do not call others are called “leaf procedure”
However, not any procedure is “leaf procedure.”
Nested Procedure Example:
int sumSquare(int x, int y) { return mult(x,x)+ y; }
Something called sumSquare, now sumSquare is calling mult.
So there’s a value in $ra that sumSquare wants to jump back to, but this will be overwritten by the call to mult.
Need to save sumSquare return address before call to mult.

## Slide 129: Nested Procedures (2/2)
In general, may need to save some other info in addition to $ra.
When a C program is run, there are 3 important memory areas allocated:
  Static: Variables declared once per program, cease to exist only after execution completes. E.g., C globals
  Heap: Variables declared dynamically
  Stack: Space to be used by procedure during execution; this is where we can save register values

## Slide 130: MIPS Memory Allocation
MIPS Machine Program
Variables declared
once per program
heap: Explicitly created
space, e.g., malloc
Space for saved procedure information

## Slide 131: Example: Using the Stack (1/2)
So we have a register $sp which always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
  int sumSquare(int x, int y) { return mult(x,x)+ y; }

## Slide 132: Example: Using the Stack (2/2)
MIPS
sumSquare: addi $sp,$sp,-8 # space on stack sw $ra, 4($sp) # save ret addr sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x) jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y lw $ra, 4($sp) # get ret addr addi $sp,$sp,8 # restore stack
jr $ra mult: ...
  C Code: int sumSquare(int x, int y) { return mult(x,x)+ y; }
“push”
“pop”

## Slide 133: Steps for Making a Procedure Call
Saves unpreserved registers it expects to use ($a0 - $a3, $t0 - $t9) after called procedure returns.
Assign argument(s) to $a0-$a3, if any.
jal call
Restore values from stack.

## Slide 134: Rules for Procedures
Called with a jal instruction, returns with a jr $ra
Accepts up to 4 arguments in $a0, $a1, $a2 and $a3
Return value is always in $v0 (and if necessary in $v1)
Must follow register conventions (even in functions that only you will call)!

## Slide 135: Basic Structure of a Function
entry_label: addi $sp,$sp, -framesize sw $ra, framesize-4($sp) # save $ra save other regs if need be
...
restore other regs if need be lw $ra, framesize-4($sp) # restore $ra addi $sp,$sp, framesize jr $ra
Epilogue
Prologue
Body (call other functions…)
ra
memory
Notes: Do example on pp. 81 and 83

## Slide 136: MIPS Registers
The constant 0 $0 $zero Reserved for Assembler $1 $at Return Values $2-$3 $v0-$v1 Arguments $4-$7 $a0-$a3 Temporary $8-$15 $t0-$t7 Saved $16-$23 $s0-$s7 More Temporary $24-$25 $t8-$t9 Used by Kernel $26-27 $k0-$k1 Global Pointer $28 $gp Stack Pointer $29 $sp Frame Pointer $30 $fp Return Address $31 $ra
Use names for registers -- code is clearer!

## Slide 137: Other Registers
$at: may be used by the assembler at any time; unsafe to use
$k0-$k1: may be used by the OS at any time; unsafe to use
$gp, $fp: don’t worry about them
Note: Feel free to read up on $gp and $fp, but you can write perfectly good MIPS code without them.

## Slide 138: A More Challenging MIPS Procedure
How to implement the following procedure which calculates factorial?
  Int fact (int n)
  {
  if (n<1) return (1);
  else return (n*fact(n-1));
  }

## Slide 139: The complied MIPS code
fact:
addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra

## Slide 140: Review on MIPS Procedure
Functions called with jal, return with jr $ra.
The stack is your friend: Use it to save anything you need. Just be sure to leave it the way you found it.
Instructions we know so far
  Arithmetic: add, addi, sub, addu, addiu, subu
  Memory: lw, sw, lb, sb, lbu, lui
  Decision: beq, bne, slt, slti, sltu, sltiu
  Logical and Shifting: and, or, nor, andi, ori, sll, srl
  Unconditional Branches (Jumps): j, jal, jr
Registers we know so far
  All of them!
  There are CONVENTIONS when calling procedures!

## Slide 141: A More Challenging MIPS Procedure
How to implement the following procedure which calculates factorial?
  Int fact (int n)
  {
  if (n<1) return (1);
  else return (n*fact(n-1));
  }

## Slide 142: The complied MIPS code
fact:
addi $sp, $sp, -8 #save space for 2 words
sw $ra, 4($sp) #save return address
sw $a0, 0($sp) #save argument
slti $t0, $a0, 1 # test for n < 1
beq $t0, $zero, L1
addi $v0, $zero, 1 # if so result is 1
addi $sp, $sp, 8 # pop 2 words from stack
jr $ra # and return
L1: addi $a0, $a0, -1 # else decrement n
jal fact # recursive call
lw $a0, 0($sp) # restore original n
lw $ra, 4($sp) # and return address
addi $sp, $sp, 8 # pop two items from stack
mul $v0, $a0, $v0 # multiply to get result
jr $ra # and return

## Slide 143: Stack Allocation before, during, and after the procedure call.
before
during
after

## Slide 144: Register Conventions (1/4)
CalleR: the calling function
CalleE: the function being called
When callee returns from executing, the caller needs to know which registers may have changed and which are guaranteed to be unchanged.
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (jal) and which may be changed.

## Slide 145: Register Conventions (2/4) - saved
$0: No Change. Always 0.
$s0-$s7: Restore if you change. Very important, that’s why they’re called saved registers. If the callee changes these in any way, it must restore the original values before returning.
$sp: Restore if you change. The stack pointer must point to the same place before and after the jal call, or else the caller won’t be able to restore values from the stack.
HINT -- All saved registers start with S!

## Slide 146: Register Conventions (3/4) - volatile
$ra: Can Change. The jal call itself will change this register. Caller needs to save on stack if nested call.
$v0-$v1: Can Change. These will contain the new returned values.
$a0-$a3: Can change. These are volatile argument registers. Caller needs to save if they’ll need them after the call.
$t0-$t9: Can change. That’s why they’re called temporary: any procedure may change them at any time. Caller needs to save if they’ll need them afterwards.

## Slide 147: Register Conventions (4/4)
What do these conventions mean?
  If function R calls function E, then function R must save any temporary registers that it may be using onto the stack before making a jal call.
  Function E must save any S (saved) registers it intends to use before garbling up their values
  Remember: Caller/callee need to save only temporary/saved registers they are using, not all registers.

## Slide 148: Parents leaving for weekend analogy (1/5)
Parents (main) leaving for weekend
They (caller) give keys to the house to kid (callee) with the rules (calling conventions):
  You can trash the temporary room(s), like the den and basement (registers) if you want, we don’t care about it
  BUT you’d better leave the rooms (registers) that we want to save for the guests untouched. “these rooms better look the same when we return!”

## Slide 149: Parents leaving for weekend analogy (2/5)
Kid now “owns” rooms (registers)
Kid wants to use the saved rooms for a wild, wild party (computation)
What does kid (callee) do?
  Kid takes what was in these rooms and puts them in the garage (memory)
  Kid throws the party, trashes everything (except garage, who goes there?)
  Kid restores the rooms the parents wanted saved after the party by replacing the items from the garage (memory) back into those saved rooms

## Slide 150: Parents leaving for weekend analogy (3/5)
Same scenario, except before parents return and kid replaces saved rooms…
Kid (callee) has left valuable stuff (data) all over.
  Kid’s friend (another callee) wants the house for a party when the kid is away
  Kid knows that friend might trash the place destroying valuable stuff!
  Kid remembers rule parents taught and now becomes the “heavy” (caller), instructing friend (callee) on good rules (conventions) of house.

## Slide 151: Parents leaving for weekend analogy (4/5)
If kid had data in temporary rooms (which were going to be trashed), there are three options:
  Move items directly to garage (memory)
  Move items to saved rooms whose contents have already been moved to the garage (memory)
  Optimize lifestyle (code) so that the amount you’ve got to ship stuff back and forth from garage (memory) is minimized
Otherwise: “Dude, where’s my data?!”

## Slide 152: Parents leaving for weekend analogy (5/5)
Friend now “owns” rooms (registers)
Friend wants to use the saved rooms for a wild, wild party (computation)
What does friend (callee) do?
  Friend takes what was in these rooms and puts them in the garage (memory)
  Friend throws the party, trashes everything (except garage)
  Friend restores the rooms the kid wanted saved after the party by replacing the items from the garage (memory) back into those saved rooms

## Slide 153: How Computer Communicate with People?
ASCII Code (8 bits per character):
Corresponding MIPS Instruction:
  load byte: lb $t0, 0($sp)
  save byte: sb $t0, 0($gb)
Unicode (16 bits per character)
Corresponding MIPS Instruction:
  load half: lh $t0, 0($sp)
  save half: sh $t0, 0($sp)

## Slide 154: ASCII Table

## Slide 155: MIPS Program Example: How to use ASCII code to represent a string?
.text
.globl main
main: li $v0, 4
la $a0, str1
syscall
li $v0, 4
la $a0, str2
syscall
li $v0, 10
syscall # exit
.data
str1:.asciiz "The quick brown fox jumps over the lazy dog\n"
str2:.byte 84, 104, 101, 32, 113, 117, 105, 99
.byte 107, 32, 98, 114, 111, 119, 110, 32
.byte 102, 111, 120, 32, 106, 117, 109, 112
.byte 115, 32, 111, 118, 101, 114, 32, 116
.byte 104, 101, 32, 108, 97, 122, 121, 32
.byte 100, 111, 103, 10, 0

## Slide 156: ASCII Poem
^<@<.@*
  }"_# |
  -@$&/_%
  !( @|=>
  ;`+$?^?
  ,#"~|)^G
hat less at less point at star
backbrace double base pound space bar
dash at cash and slash base rate
wow open tab at bar is great
semi backquote plus cash huh DEL
comma pound double tilde bar close BEL

## Slide 157: Review of MIPS Format
Simple instructions all 32 bits wide
Very structured, no unnecessary baggage
Only three instruction formats
Rely on compiler to achieve performance — what are the compiler's goals?
Help compiler when we can
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 158: Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Formats: Address fields are not 32 bits — How do we handle this with load and store instructions?
op rs rt 16 bit address
op 26 bit address
I
J

## Slide 159: Branches: PC-Relative Addressing (1/5)
Use I-Format
opcode
rs
rt
immediate
opcode specifies beq v. bne
rs and rt specify registers to compare
What can immediate specify?
  immediate is only 16 bits
  PC (Program Counter) has byte address of current instruction being executed; 32-bit pointer to memory
  So immediate cannot specify entire address to branch to.

## Slide 160: Program Counter in a MIPS Computer

## Slide 161: Branches: PC-Relative Addressing (2/5)
How do we usually use branches?
  Answer: if-else, while, for
  Loops are generally small: typically up to 50 instructions
  Function calls and unconditional jumps are done using jump instructions (j and jal), not the branches.
Conclusion: may want to branch to anywhere in memory, but a branch often changes PC by a small amount

## Slide 162: Branches: PC-Relative Addressing (3/5)
Solution to branches in a 32-bit instruction: PC-Relative Addressing
Let the 16-bit immediate field be a signed two’s complement integer to be added to the PC if we take the branch.
Now we can branch ± 215 bytes from the PC, which should be enough to cover almost any loop.

## Slide 163: Branches: PC-Relative Addressing (4/5)
Note: Instructions are words, so they’re word aligned (byte address is always a multiple of 4, which means it ends with 00 in binary).
  So the number of bytes to add to the PC will always be a multiple of 4.
  So specify the immediate in words.
Now, we can branch ± 215 words from the PC (or ± 217 bytes), so we can handle loops 4 times as large.

## Slide 164: Branches: PC-Relative Addressing (5/5)
Branch Calculation:
  If we don’t take the branch:
  PC = PC + 4
  PC+4 = byte address of next instruction
  If we do take the branch:
  PC = (PC + 4) + (immediate * 4)
  Observations
    Immediate field specifies the number of words to jump, which is simply the number of instructions to jump.
    Immediate field can be positive or negative.
    Due to hardware, add immediate to (PC+4), not to PC; will discuss next semester

## Slide 165
Summary
We discussed about team project requirements today
Review 210 course syllabus today