## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 13
September 24, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover Circuits and Number Systems
We will begin to cover how to do math in the binary format and how to implement it in hardware
The binary math we learn will be used to build arithmetic logic unit (ALU)
Quiz 2 grades and key are posted on Blackboard
  Mean: 8.86
  Median: 9.00
  Standard Deviation: 1.52
  Variance: 2.30
Grades and Key for Homework 2 are posted on Blackboard as well
We will have our Exam 1 on Friday, October 5, 2018

## Slide 3: Where are we?
So far, we covered the following topics
  Fundamental digital blocks: AND, OR, and NOT gates.
  Boolean algebra.
  Base conversion between different number bases.
We will begin to cover how to do math in the binary format and how to implement it in hardware.
The binary math we learn will be used to build arithmetic logic unit (ALU).

## Slide 4: ALU in a MIPS Computer
ALU

## Slide 5: Binary Addition with Pencil and Paper
1001
1111
11000
1111
Augend
Addend
Sum
Carry In
Carry Out
1111
+)

## Slide 6: Functional Block: Half-Adder
A 2-input, 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce a two-bit sum
The sum is expressed as a sum bit , S
and a carry bit, C
The half adder can be specified
as a truth table for S and C 
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 0
0 1
0 1
1 0
X
Y
C
S
0
0
0
0
0
1
0
1
1
0
0
1
1
1
1
0
Can you identify the logic expression
of C and S with X and Y as inputs?

## Slide 7: Implementations: Half-Adder
The most common half adder implementation is:
Y
X
C
Y
X
S
×
=
Å
=
X
Y
C
S

## Slide 8: Functional Block: Full-Adder
A full adder is similar to a half adder, but includes a carry-in bit from lower stages. Like the half-adder, it computes a sum bit, S and a carry bit, C.
  For a carry-in (Z) of 0, it is the same as the half-adder:
  For a carry- in (Z) of 1:
Z
0
0
0
0
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0
0
0 1
0 1
1 0
Z
1
1
1
1
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 1
1 0
1 0
1
1

## Slide 9: Implementation: Full Adder
Full Adder Schematic
Z
Y
X
S
Å
Å
=
Z
)
Y
X
(
Y
X
C
Å
+
=

## Slide 10: Binary Adders
To add multiple operands, we “bundle” logical signals together into vectors and use functional blocks that operate on the vectors
Example: 4-bit ripple carry adder: Adds input vectors A(3:0) and B(3:0) to get a sum vector S(3:0)
Note: carry out of cell i becomes carry in of cell i + 1
Description
Subscript
3 2 1 0
Name
Carry In
0 1 1 0
Ci
Augend
1 0 1 1
Ai
Addend
0 0 1 1
Bi
Sum
1 1 1 0
Si
Carry out
0 0 1 1
Ci+1

## Slide 11: 4-bit Ripple-Carry Binary Adder
A four-bit Ripple Carry Adder made from four 1-bit Full Adders is shown below.
One problem with the addition of binary numbers is the length of time to propagate the ripple carry from the least significant bit to the most significant bit. (Solution: look ahead adder.)

## Slide 12: In-Class Exercise
Perform the following binary addition:
  0011+1001
  1110+0011

## Slide 13: Sign Integer
In elementary school math, we use “+” to indicate a positive number, and “-” to indicate a negative number.
Since the computer can only identify 0 and 1, we use 0 and 1 to indicate positive and negative numbers.

## Slide 14: Signed and Unsigned Integers
Three possible representations might be applied:
  Signed Magnitude: Use 1 bit to present the sign of number (0: positive, 1: negative).
  One’s Compliment: For n-bit number, use (2n-1-K) to represent number -K
  Two’s Compliment: For n-bit number, use (2n-K) to represent number -K

## Slide 15: Possible Representations
Assume that three bits are used to present signed integer. The followings are the signed integer presented by three signed integer systems.
Sign Magnitude One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Which one is best? Why?

## Slide 16: Representation Range of n-bit Signed Integer (2’s Complement)
For a n-bit signed integer represented with 2’s complement, its range is -2n-1~2n-1-1
Note: for -2n-1, its 2’s complement binary representation is
10  002
N-1 of zeros
If you take two’s complement of this number
you will get the same sequences!

## Slide 17: Signed Integer in MIPS
32 bit signed numbers: 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten 0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0010two = – 2,147,483,646ten ... 1111 1111 1111 1111 1111 1111 1111 1101two = – 3ten 1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint

## Slide 18: 2’s Complement Representation
For a positive number: “0” is added in the beginning of the number
  11510=011100112
For a negative number:
  11510 = 011100112, we use 8 bits to present a number, then we have:
  (28 ) = 25610 or 1000000002
  The 2's complement of 01110011 is then:
  1000000002 -) 011100112 100011012
The alternative method: invert all bits and add 1.