## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 14
September 26, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover Circuits and Number Systems
We will begin to cover how to do math in the binary format and how to implement it in hardware
The binary math we learn will be used to build arithmetic logic unit (ALU)
Quiz 2 grades and key are posted on Blackboard
Grades and Key for Homework 2 are posted on Blackboard as well
We will have one more quiz before our exam 1 [(quiz 3) on Wednesday, October 3], which will be on lectures 10-15
We will have our Exam 1 on Friday, October 5, 2018, which will be on lecture 1-15

## Slide 3: Review: Signed and Unsigned Integers
Three possible representations might be applied:
  Signed Magnitude: Use 1 bit to present the sign of number (0: positive, 1: negative).
  One’s Compliment: For n-bit number, use (2n-1-K) to represent number -K
  Two’s Compliment: For n-bit number, use (2n-K) to represent number -K

## Slide 4: Possible Representations
Assume that three bits are used to present signed integer. The followings are the signed integer presented by three signed integer systems.
Sign Magnitude One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Which one is best? Why?

## Slide 5: Representation Range of n-bit Signed Integer (2’s Complement)
For a n-bit signed integer represented with 2’s complement, its range is -2n-1~2n-1-1
Note: for -2n-1, its 2’s complement binary representation is
10  002
N-1 of zeros
If you take two’s complement of this number
you will get the same sequences!

## Slide 6: Signed Integer in MIPS
32 bit signed numbers: 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten 0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0010two = – 2,147,483,646ten ... 1111 1111 1111 1111 1111 1111 1111 1101two = – 3ten 1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint

## Slide 7: 2’s Complement Representation
For a positive number: “0” is added in the beginning of the number
  11510=011100112
For a negative number:
  11510 = 011100112, we use 8 bits to present a number, then we have:
  (28 ) = 25610 or 1000000002
  The 2's complement of 01110011 is then:
  1000000002 -) 011100112 100011012
The alternative method: invert all bits and add 1.

## Slide 8
Unsigned Binary Arithmetic
Base-2 addition - just like base-10
- add from right to left, propagating carry
10010
+ 1001
11011
carry
10010
+ 1011
11101
1111
+ 1
10000

## Slide 9
Unsigned Binary Arithmetic Practice
Base-2 addition - just like base-10 - add from right to left, propagating carry
Subtraction, multiplication, division...
10111
+ 1111
10101
+ 1111

## Slide 10: Two's Complement
Two's complement representation was developed to make circuits easy for arithmetic.
-for each positive number (X), assign value to its negative (-X), such that X + (-X) = 0 with "normal" addition, ignoring carry out
00101 | (5) | 01001 | (9)
+ 11011 | (-5) | + | (-9)
00000 | (0) | 00000 | (0)

## Slide 11: Two's Complement
If number is positive or zero,
  normal binary representation, zeroes in upper bit(s)
If number is negative,
  start with positive number
  flip every bit (i.e., take the one’s complement)
  then add one
 | 00101 | (5) |  |  | 01001 | (9)
 | 11010 | (1’s comp) |  |  |  | (1’s comp)
+ | 1 |  |  | + | 1 | 
 | 11011 | (-5) |  |  |  | (-9)

## Slide 12: Two’s Complement Signed Integers
Most Significant bit is sign bit – it has weight –2n-1.
Range of an n-bit number: -2n-1 through 2n-1 – 1.
The most negative number (-2n-1) has no positive counterpart.
-23 22 21 20 -23
22 21 20
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | -8
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | -7
0 | 0 | 1 | 0 | 2 | 1 | 0 | 1 | 0 | -6
0 | 0 | 1 | 1 | 3 | 1 | 0 | 1 | 1 | -5
0 | 1 | 0 | 0 | 4 | 1 | 1 | 0 | 0 | -4
0 | 1 | 0 | 1 | 5 | 1 | 1 | 0 | 1 | -3
0 | 1 | 1 | 0 | 6 | 1 | 1 | 1 | 0 | -2
0 | 1 | 1 | 1 | 7 | 1 | 1 | 1 | 1 | -1

## Slide 13: Converting Binary (2’s C) to Decimal
If leading bit is one, take two’s complement to get a positive number.
Add powers of 2 that have “1” in the corresponding bit positions.
If original number was negative, add a minus sign.
X = 01101000two
= 26+25+23 = 64+32+8
= 104ten
Assuming 8-bit 2’s complement numbers.
n 0 1 | 2n 1 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
(K) 10 | 1024
(M) 20 | 1048576

## Slide 14: More Examples
X = 00100111two
= 25+22+21+20 = 32+4+2+1
= 39ten
X = 11100110two
-X = 00011010
= 24+23+21 = 16+8+2
= 26ten X = -26ten
Assuming 8-bit 2’s complement numbers.
n 0 1 | 2n 1 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
(K) 10 | 1024
(M) 20 | 1048576

## Slide 15: Operations: Arithmetic
Recall: A data type includes representation and operations. We now have a good representation for signed integers, so let’s look at some arithmetic operations:
Addition
Subtraction
Sign Extension

## Slide 16: Addition
As we’ve discussed, 2’s comp. addition is just binary addition.
assume all integers have the same number of bits
ignore carry out
for now, assume that sum fits in n-bit 2’s comp. representation
Assuming 8-bit 2’s complement numbers.
01101000 | (104) |  | 11110110 (-10)
+ 11110000 | (-16) | + | (-9)
01011000 | (88) |  | (-19)

## Slide 17: In-Class Exercises
Represent the following numbers as two’s complement binary numbers (8 bits):
  13
  -12
Determine the value of the following numbers assuming they are 2’s complement binary number:
  100011112
  000000112

## Slide 18: Sign Extension
T o add two numbers, we must represent them with the same number of bits.
If we just pad with zeroes on the left:
Instead, replicate the most significant bit -- the sign bit:
4-bit |  | 8-bit | 
0100 | (4) | 00000100 | (still 4)
1100 | (-4) | 00001100 | (12, not -4)
4-bit |  | 8-bit | 
0100 | (4) | 00000100 | (still 4)
1100 | (-4) | 11111100 | (still -4)

## Slide 19: Sign Extension
Converting n bit numbers into numbers with more than n bits:
  copy the most significant bit (the sign bit) into the other bits:
  Sign Extension 0010 -> 0000 0010 1010 -> 1111 1010

## Slide 20: Unsigned 2’s Complement Subtraction Example
Subtraction using addition of negative numbers
Find 010101002 – 010000112
01010100 01010100
– 01000011 + 10111101
100010001
The carry of 1 indicates that no correction of the result is required. (We will talk more about it when we cover overflow issue)
2’s comp

## Slide 21: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 22: Summary
Today, we begin to cover the following important concepts:
  2’s complement
  How to use 2’s complement to do subtraction
  The implementation of subtraction
We will cover the overflow problem and its detection in great details the next time.
Reading Materials: Appendix C.5, Chapter 2.4, 3.2