## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 15
September 28, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover how to do math in the binary format and how to implement it in hardware
  2’s complement
  Overflow problems
  Multiplications and Divisions
  Decoder and Multiplexer
Homework 3 is posted on Blackboard which is due on Wednesday, October 3 at the beginning of the class
We will have one more quiz before our exam 1 [(quiz 3) on Wednesday, October 3], which will be on lectures 10-15
We will have our Exam 1 on Friday, October 5, 2018, which will be on lecture 1-15
A sample exam with key will post on Blackboard on next week

## Slide 3: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 4: More about 2’s Complement
How can we be sure that addition/subtraction with 2’s complement representation generates correct answer?
For a n-bit signed integer, 2n-k represent -k
  2’s complement of (–k)=2n– (2n–k)=k
  A–B=(A)+(2n–B)=2n–(B–A)
    If B>A, the result is 2’s complement of (B–A), i.e. –(A–B),
    If A>B, there is one extra bit at n+1 bit position which should be discarded.
  If the result is outside (-2n-1, 2n-1 -1), then, overflow happens

## Slide 5: In-Class Exercise
Perform the following calculation with 2’s complement math. Give your result in binary number. Each number has 8 bits.
  1510-2410
  -3210+4510

## Slide 6: Overflow Problem
Consider the following calculation:
  10000100
  +) 11110011
  101110111
The sum of two negative numbers equal to a positive number!!! We got a problem. It is called the overflow problem which happens when the calculation result is outside the range.
We are going to cover it in great details.

## Slide 7: Overflow
Overflow occurs when the resulting value of an operation performed on valid representations of numbers is out of the range of valid values
How overflow occurs depends:
the operation being performed
the representation system used to represent the numbers,
and the number of bits used
Realize that the representation system is important!!

## Slide 8: Overflow detection in Unsigned Binary (UB)
If you are representing numbers using 4 bits as UB minimum value = 00002 = 010
maximum value = 11112 = 1510
Why not just use 5 bits? Hardware limitations!
 | 1 | 4
+ | 1 | 4
 | 2 | 8
 | 1 | 1 | 1 | 0
+ | 1 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0

## Slide 9: Overflow Problem
Overflow happens, when the calculation result is beyond the representation range.
When might overflow happen?
  Positive + Positive
  Negative + Negative
  Positive – Negative
  Negative – Positive

## Slide 10: Overflow Detection Method 1
If one of the following situations happens, then there is an overflow.
  Positive + Positive  Negative
  Negative + Negative  Positive
  Positive – Negative  Negative
  Negative – Positive  Positive
When overflow happens, different programming languages behave differently.
  C: Ignore
  Fortran: Notify the program

## Slide 11: Overflow Detection Method 2 (I)
Overflow occurs if n + 1 bits are required to contain the result from an n-bit addition or subtraction
Overflow can occur for:
  Addition of two operands with the same sign
  Subtraction of operands with different signs
Signed number overflow cases with correct result sign
Detection can be performed by examining the result signs which should match the signs of the top operand

## Slide 12: Overflow Detection Method 2 (II)
Signed number cases with carries shown for erroneous result signs (indicating overflow):
Carry Out 01 10
0 1 + 0 +1 1 0
Simplest way to implement overflow V = Cn + Cn + 1
Example: Add +69 (0 1000101) with +78 (0 1001110) ------- Carries: 01
    Add -69 (1 0111011) with -78 (1 0110010) ------- Carries: 10

## Slide 13: An Add-Subtractor with the Overflow Detection
Overflow Detection

## Slide 14: Overflow Examples
Perform the following calculation and detect if overflow happens
  111000112+100111002
  000111112-100000002
  001111112+100011112

## Slide 15: Summary
We started discussing the Overflow today.
We will have quiz 3 and exam 1 next week.