## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 9
September 14, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will continue to cover Number Systems
Will discuss:
  Number Systems Conversion
  Fractional Number Systems
  We will begin to cover how to do math in the binary format and how to implement it in hardware
Homework 2 is posted on blackboard which is due on Wednesday, September 19 at the beginning of the lecture (Hard Copy)
We will have quiz 2 on Friday, September 21, which will cover lectures 5-9

## Slide 3: Binary to Decimal Conversion
···b3b2b1b0 (each bit bi is 0 or 1)
b0×20 + b1×21 + b2×22 + b3×23 + ···
= b0×1 + b1×2 + b2×4 + b3×8 + ···
Binary Number:
Its decimal value is:
Examples: 11102 Decimal value is:
11112 Decimal value is:
1100102 Decimal value is:
1111112 Decimal value is:
Check your understanding:
N bits  2N combinations  decimal numbers 0, 1, 2, 3, …, 2N - 1
The largest number: 11…112 = 2N-1 (decimal)
14
15
50
63
N bits, all ones

## Slide 4: Converting Binary to Decimal
To convert to decimal, use decimal arithmetic to form S (digit × respective power of 2).
Example 2: Convert 110102 to N10:
N= 124+123+022+121+020=26
Example 3: Convert 10.112 to R10
R= 121+020+12-1+12-2=2.75
Binary number: 0.b-1b-2b-3b-4···
Decimal value: b-1×2-1 + b-2×2-2 + b-3×2-3 + b-4×2-4 + ···
Notes: Powers of 2: 43210
110102 =>
1 X 24 = 16
+ 1 X 23 = 8
+ 0 X 22 = 0
+ 1 X 21 = 2
+ 0 X 20 = 0
2610

## Slide 5: In-Class Exercise
Converting the following binary number to decimal number:
  10112
  110.0112

## Slide 6: Decimal to Binary Conversion
LSB
MSB
Example: Decimal number 39
Divide 39 by 2 = 19 + remainder 1
Divide 19 by 2 = 9 + remainder 1
Divide 9 by 2 = 4 + remainder 1
Divide 4 by 2 = 2 + remainder 0
Divide 2 by 2 = 1 + remainder 0
Divide 1 by 2 = 0 + remainder 1
Binary representation: 100111
Procedure: Successive division by 2
Divide the decimal number by 2 & record the quotient & remainder.
Repeat step 1 with the quotient from the previous step. Stop when quotient = 0.
The remainders give the binary representation, starting with the rightmost or least significant bit (LSB) and ending with the leftmost or most significant bit (MSB).

## Slide 7: In-Class Exercise
Converting the following decimal integers to binary numbers:
  1310
  11110

## Slide 8: Commonly Occurring Bases
Name
Radix
Digits
Binary
2
0,1
Octal
8
0,1,2,3,4,5,6,7
Decimal
10
0,1,2,3,4,5,6,7,8,9
Hexadecimal
16
0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
The six letters (in addition to the 10
integers) in hexadecimal represent: 11 12 13 14 15
Notes: Answer: The six letters A, B, C, D, E, and F represent the digits for values
10, 11, 12, 13, 14, 15 (given in decimal), respectively, in hexadecimal.
Alternatively, a, b, c, d, e, f are used.

## Slide 9: Hexadecimal (Hex) Representation
Uses 16 symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
To convert hex to decimal: Hex #: ···MNOP → dec. value = P10×160 + O10×161 + N10×162 + M10×163 + ···
Notation: 5C416 or 0x5C4. Each digit represents the coefficient of a power of 16, as indicated below.
Digits A, B, C, D, E, F represent the decimal numbers 10, 11, 12, 13, 14, 15, respectively.

## Slide 10: Decimal and Binary Values of Hex Digits
Hex digit | Decimal value | Binary value
0 1 2 3 | 0 1 2 3 | 0000 0001 0010 0011
4 5 6 7 | 4 5 6 7 | 0100 0101 0110 0111
Hex digit | Decimal value | Binary value
8 9 A B | 8 9 10 11 | 1000 1001 1010 1011
C D E F | 12 13 14 15 | 1100 1101 1110 1111
Example: Convert 6E416 to decimal.
Answer: 6E416 = 4×160 + 14×161 + 6×162 = 1764

## Slide 11: Other Conversions
Convert decimal to hex
Use the successive division method described previously (for decimal to binary), but divide by 16 instead of 2.
Convert binary to hex
  A hex digit is equivalent to 4 bits.
  Divide binary number into groups of 4 bits, starting from the right.
  Convert each 4 bit group into one hex digit.
Convert hex to binary
  Convert each hex digit to its 4-bit binary equivalent.
  String the bits together.
Note: Computationally, it’s easy to convert between bases that are powers of 2, as indicated in the binary to hex conversion technique above.

## Slide 12: Other Conversions
Convert decimal to Octal
Use the successive division method described previously (for decimal to binary), but divide by 8 instead of 2.
Convert binary to Octal
  A octal digit is equivalent to 3 bits.
  Divide binary number into groups of 3 bits, starting from the right.
  Convert each 3 bit group into one octal digit.
Convert octal to binary
  Convert each octal digit to its 3-bit binary equivalent.
  String the bits together.
(examples on next slide)

## Slide 13: Examples
2. Convert 11100111001012 to hex.
4. Convert 32BD16 to decimal.
5. Convert 102410 to hex.
3. Convert 32BD16 to binary.
1. Convert 5416 to decimal.
Answer: 5416 = 4×160 + 5×161 =
32BD16 = 13×160 + 11×161 + 2×162 + 3×163 =
1
C
E
5
3 2 B D
11
→ 1CE516
8410
0010
1011
11012
1298910
1024/16 = 64, R=0
64/16 = 4, R=0
4/16 = 0, R=4
→ 40016
6. Convert 9810 to Octal.
1428

## Slide 14: More Example: Convert 1011.01112 to Decimal
Convert 10112 to Decimal Number
Convert 0.01112 to Decimal Number :
Join the results together with the radix point:
Notes: Answer 1: Converting 46 as integral part: Answer 2: Converting 0.6875 as fractional part:
46/2 = 23 rem = 0 0.6875 * 2 = 1.3750 int = 1
23/2 = 11 rem = 1 0.3750 * 2 = 0.7500 int = 0
11/2 = 5 remainder = 1 0.7500 * 2 = 1.5000 int = 1
5/2 = 2 remainder = 1 0.5000 * 2 = 1.0000 int = 1
2/2 = 1 remainder = 0 0.0000
1/2 = 0 remainder = 1 Reading off in the forward direction: 0.10112
Reading off in the reverse direction: 1011102
Answer 3: Combining Integral and Fractional Parts:
101110. 10112

## Slide 15: In-Class Exercises
Convert 43.12510 to a binary number
Convert 1101.10112 to hexadecimal number

## Slide 16: Summary
We discussed our coverage on digital logic with which we built a very simple processor
We will have quiz 2 on Friday, September 21