## Slide 1: CSCIU 210 Computer Organization AKM Jahangir A Majumder, PhD
Fall 2018 - Lecture 19
October 10, 2018
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We finished our coverage on Multiplexer, Demultiplexer
We will start to cover simple ALU design today.
  build a 32-bit ALU
  and, or, nor, add, subtract, and slt (set on less than)
Exam 1 grades and Keys are posted on Blackboard
HW 3 grades are posted on Blackboard
We will have Quiz 4 on Wednesday, October 17, which will cover lecture 16-19
HW 4 will post on Blackboard soon
No Class on Friday, October 12

## Slide 3: Summary of Materials We Covered up to Now
So far, we covered the following important concepts:
  Fundamental Logic Gates and Some Important Logic Components
    Decoder and Multiplexer.
  Boolean Algebra
  Number Representation with Different Bases
    Decimal, Binary, Hexadecimal, Octal.
  Binary Addition and Subtraction with the 2’s complement
    Overflow Detection
We are going to use the concepts we covered up to now to build a simple ALU (Arithmetic Logical Unit)

## Slide 4: ALU Functions
We want to build a 32-bit ALU which can perform the following operations:
  and, or, nor, add, subtract, and slt (set on less than)
32
32
32
operation
result
a
b
ALU

## Slide 5: An ALU (arithmetic logic unit)
Let's build an ALU to support the ‘and’ and ‘or’ functions at the first.
  we'll just build a 1 bit ALU, and use 32 of them
Possible Implementation (sum-of-products):
a
b
ALU
operation
result
op
a
b
res

## Slide 6: Review: The Multiplexor
Selects one of the inputs to be the output, based on a control input
Lets build our ALU using a MUX:
S
C
A
B
0
1
note: we call this a 2-input mux even though it has 3 inputs!

## Slide 7: The one-bit ALU Implementation with a MUX
0
1
S (Operation)
C
A
B
A+B
AB
S=0 Output, c =(AB)
S=1  Output, c=(A+B)

## Slide 8: Different Implementations
Not easy to decide the “best” way to build something
  Don't want too many inputs to a single gate
  Don’t want to have to go through too many gates
  For our purposes, ease of comprehension is important
Let's look at a 1-bit ALU for addition: How could we build a 1-bit ALU for ‘add’, ‘and’, and ‘or’?
How could we build a 32-bit ALU?

## Slide 9: Review: 1 bit Full Adder Implementation
cin
b
a
sum
Å
Å
=
cin
)
b
a
(
b
a
cout
Å
+
=
a
b
carry in
carry out
sum

## Slide 10: Review: Functional Block of Full-Adder
A full adder is similar to a half adder, but includes a carry-in bit from lower stages. Like the half-adder, it computes a sum bit, S and a carry bit, C.
  For a carry-in (Z) of 0, it is the same as the half-adder:
  For a carry- in (Z) of 1:
Z
0
0
0
0
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0
0
0 1
0 1
1 0
Z
1
1
1
1
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 1
1 0
1 0
1
1

## Slide 11: 1-bit Full Adder Symbol

## Slide 12: Building a 32 bit ALU with ‘and,’ ‘or,’ and ‘add’ Functions
How many bits do we need to represent ‘operation’?

## Slide 13: What about subtraction (a – b) ?
Two's complement approach: just negate b and add.
How do we negate?
A very clever solution:
  Invert every bit of bi
  Set Carry in as 1 for the
  Least Significant Bit (LSB).
We are going to cover
how to wire inputs later.

## Slide 14: Review: Least Significant Bit and Most Significant Bit
1000 0011 0011 0011 1101 1010 0011 0011
Most Significant Bit
(MSB)
Least Significant Bit
(LSB)

## Slide 15: Adding a NOR function
A nor function can be represented as (A+B)’=A’B’ (It is called DeMorgan’s law)
A | B | (A+B)’ | A’B’
0 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0

## Slide 16: DeMorgan’s law
(A+B)’=A’B’
(AB)’=A’+B’ (Prove it with truth table!)

## Slide 17: The NOR Function Implementation
Suppose that we can also choose to invert a. How do we get “a NOR b” ?

## Slide 18: Set-on-less-than (slt) Function
Set-on-less-than (slt) is an important MIPS functions.
The MIPS command,
‘slt $s1, $s2, $s3,’ means
  If ($s2 < $s3), then $s1=1 else $s1=0.

## Slide 19: slt Function Implementation
Our ALU needs to support the set-on-less-than instruction (slt)
  remember: slt is an arithmetic instruction
  produces a 1 if a < b and 0 otherwise
  use subtraction: (a-b) < 0 implies a < b
We can also support equality test
  use subtraction: (a-b) = 0 implies a = b

## Slide 20: Slt Function Implementation
11
Perform a-b
Output MSB from ALU 31 to ALU 0
Op ’11’ is used to chose output
0
1
11
0
1
(ALU 31)
(ALU 0~30)

## Slide 21: An 32-bit ALU Supporting slt function

## Slide 22: The 1-bit ALU for the Most Significant Bit

## Slide 23: The 1-bit ALU for Other Bits

## Slide 24: Final 32-bit ALU with a Zero Detector
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
Note: zero is a 1 when the result is zero!

## Slide 25: Our 32-bit ALU Symbol
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR

## Slide 26: The ALU Diagram
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
ALU 0~30
ALU 31
Can this ALU implement a NAND function?

## Slide 27: Question regarding ALU
Among 6 functions (‘and’, ‘or’, ‘nor’, ‘add’, ‘sub’, and ‘slt’), our simple ALU capable to handle, which one takes the longest time to finish?

## Slide 28: A MIPS Computer Architecture

## Slide 29: Summary
Today, we started to cover a simple ALU design